## Slide 1: Waterwheel prototype 1 (speed)
Wheel part | Change | Description
Number of blades | High | Would likely increase speed
Interior drum | No drum | Wheel is not mid/overshot
Shape of blades | Flat | Would likely increase speed
Water direction | Undershot | Would likely increase speed
Weights | No weights | Would likely increase speed
Description:
The changes made to wheel prototype 1 are aimed at having the wheel spin as fast as possible to gauge the effects this has on the reliability of its readings.
Hypothesis:
Wheel would measure accurately the smaller changes in water-flow due to its low weight, having a greater responsiveness. However, this would come at a cost to the reliability of its readings, as the wheel would likely fluctuate in speed for the same flow rates of water due to outside factors.
Considerations for future revisions:
The increased number of blades would also likely significantly increase the weight of the wheel, negatively impacting its ability to spin fast.
CAD model:

## Slide 2: Waterwheel prototype 2 (Mid-range)
Wheel part | Change | Description
Number of blades | Medium | To allow average speed
Interior drum | No drum | Wheel is not mid/overshot
Shape of blades | Curved | Would likely increase reliability
Water direction | Undershot | Would likely increase speed
Weights | Weights | Would likely increase reliability
Description:
The changes made to wheel prototype 12 are aimed at compromising between wheel speed and reliability. This means optimizing the wheel to be heavy, yet still be fast.
Hypothesis:
The wheel would operate at an average speed, with average reliability. The balance of these two factors could make it the most accurate for making measurements of flow rate.
Considerations for future revisions:
The curve of the blades on an undershot wheel may not have any effect. The number of blades may also have to be increased to increase speed.
CAD model:

## Slide 3: Waterwheel prototype 3 (reliability)
Wheel part | Change | Description
Number of blades | High | Would likely increase speed
Interior drum | Drum | Would improve efficiency
Shape of blades | Curved | Would likely increase speed
Water direction | Mid-shot | Would improve efficiency
Weights | Many weights | Would likely improve reliability
Description:
The changes made to wheel prototype 3 are aimed at having the wheel as reliable as possible to gauge the effects this has on the reliability of its readings.
Hypothesis:
The wheel would be, by far, the most accurate and reliable for gauging flow rates for a steady rate of water, but would not be able to detect slight changes in flow rate due to increased weight. The use of mid-shot would allow the speed at which the water is travelling to have little effect as well.
Considerations for future revisions:
The number of blades being high may not make a difference. The mid-shot water direction could be more logistically difficult to implement.
CAD model:

## Slide 4: Waterwheel prototype 4 (mid-shot)
Wheel part | Change | Description
Number of blades | Medium | Would allow deep blades
Interior drum | Drum | Would improve efficiency
Shape of blades | Deep curve | Would improve efficiency
Water direction | Mid-shot | Would improve efficiency
Weights | No weights | Would likely increase speed
Description:
The changes made to wheel prototype 4 are similar to wheel 3, but the increased depth of the blade curve, as well as the decreased blade count could improve reliability.
Hypothesis:
The wheel would accurately measure the smaller changes in water flow, while also remaining reliable in gauging the overall water flow over longer periods of time.
Considerations for future revisions:
The number of blades may need to be decreased in order to have the increased depth of blades be possible.
CAD model: