WMT River System Development
Comparison of Available Devices and Protocols
# Sensor Types
This is a subset of the various sensor types that have been identified, but includes all of the viable types that do not cost more than a few tens of pounds to implement.
# Note: Analogue to Digital Converters (A/Ds) are available as detailed in the Section on Sensor Interfaces below. Unless a home made A/D is employed the costs of the commercial types must be added to the prices given in the Table below.
Device - >	HC-SR04	Probe Rods	Capacitance	Float	Pressure	Weight
Type	Level	Level	Level	Level	Level	Level
Technology	Ultrasonic Range	Conduction	Change of C	Microswitch	Air pressure	Weight of Butt
Pros	Cheap, simple, linear, existing Libraries	Cheap, simple, can use GPIO	Fairly cheap	Cheap, simple, can use GPIO	Fairly cheap, linear.	Fairly cheap, linear.
Cons	Difficult to protect from moisture/ice.	Coarse Measurement	Needs RF stimulus	Coarse Measurement	Needs pre-amp and A/D	Needs pre-amp and A/D
Price	£1.57	Home-made. A few pounds for materials. Use in case primary sensor fails.	Home-made; cost difficult to estimate. AD7745 24-bit dual capacitance conv £11.	£5 to £25, depending on the number of floats. Use in case primary sensor fails.	~£10 + A/D.	~£10 + A/D.
Order of Preference	3	1	2	1	1	4

# Sensor Types (Continued)

Device - >	VL53L0X	Paddle	Paddle	Vane	Paddle
Type	Level	Flow	Flow	Flow	Flow
Technology	Laser Range Finder	Hall Effect	Tacho-gen	Potentiometer	Optical Shaft Encoder
Pros	Linear, existing Libraries	Linear	Linear	Simple, cheap	Linear
Cons	Difficult to protect from moisture/ice		Probably have to make generator.	Non-linear, pot can wear. Needs A/D
Price	£15	~£5	?	~ £1 + A/D	~£20
Order of Preference	3	1	5	5	1

# Devices for Sensor Interfaces and Data Processing
The original version of this document suggested the Raspberry Pi A/D 'HATs' and the Arduino, which includes A/D converters as one of its many functions. After discussion on Tuesday 16th May 2017, all of these A/D devices were rejected because they are expensive and because the Arduino has far more functions than are needed for this application. The document includes them for completeness.
# It was agreed that the A/D requirements could be achieved using the MCP3008 Converter (currently ~£2 as shown after the table below.
Device - >	Raspberry Pi Zero	Raspberry Pi 3	Arduino Uno	ADC Pi Plus	ADC Pi Plus	RaspIO Analog Zero
Microcontroller	BCM2835	BCM2837 (Quad Core)	Atmega328	NS	Ditto	Ditto
Operating Voltage	5 V	5 V	5V	GPIO Header	Ditto	Ditto
Input Voltage (recd)	N/A	N/A	7-9V	NS	Ditto	Ditto
Input Voltage (limits)	N/A	N/A	6-20V	NS	Ditto	Ditto
Digital I/O Pins	26	26	14 (6 provide PWM)	GPIO (pass through)	Ditto	Ditto
Analogue Input Pins	0	0	6	8	Ditto	Ditto
Analogue Voltage Range	N/A	N/A	0 to 5 V (can be extended)	0 to 5 V	Ditto	0 to 3.3 V
Resolution (bit)	N/A	N/A	10	17	Ditto	10 (can ext to 12)
Conversion time	N/A	N/A		240 SPS	Ditto	NS
DC Current per I/O Pin	N/A	N/A	40 ma	2 mA	Ditto	NS
DC Current for 3.3V Pin	N/A	N/A	50 mA	N/A	Ditto	NS
Flash Memory	N/A	N/A	32 KB (0.5 KB bootloader)	N/A	Ditto	Ditto
SRAM	512 MB	1 GB	2 KB	N/A	Ditto	Ditto
EEPROM	NS	NS	1 KB	N/A	Ditto	Ditto
Clock Speed	1 Gb/s	1.2 Gb/s	16 MHz	NS	Ditto	Ditto
Other Features	HDMI, 1 USB Port, Camera Port	HDMI, 4 USB, Port, Camera Port, Audio Jack	2 hardware Interupts, 6 8-bit PWM O/Ps	On board Programmable Amplifier (up to 8 X)	Ditto	Small prototyping area.
Comms	1-Wire, I2C, SPI, GPIO	1-Wire, I2C, SPI, GPIO, Ethernet, 802.11n WiFi	UART, I2C, SPI	I2C	Ditto	SPI
Price	£4	£30	£11	£15.99	£14.99	£10
Order of Preference	1 as Sensor I/F	1 as Controller	X	X	X	X

# Devices for Controlling Water Movement
This table lists all of the known options for controlling the movement of water around the river system. It includes devices that are currently part of the system and other devices that might be utilised to expand the control system.

Device - >	New Sump Pump	Old Sump Pump	Solenoid Valves / (DC)	Solenoid Valves / (DC)	Solenoid Valves / (240 V AC)
Function	Move Water	Move Water	Stop Water	Divert water	Divert water
Type	Mains	Mains	2-port	3-port	3-port
Technology	PWM	Mains On-Off??	On-Off	Motorised	Motorised
Pros	Fine control possible	Free	Relatively cheap	Finer control	Finer control, Readily available
Cons		Bang-Bang control	Bang-Bang control	Not many around.	Mains
Price	Already bought	Free	£5 to £25	~£25 +	£30 to £70
Order of Preference

# Notes:
# 1. If solenoid valves alone are used to control the movement of water, then any pumps will need to be turned off when the butts or the sump are full.
# 2. If a PWM pumps are used to control the movement of water, then it will be possible to reduce the flow of water to zero, when the butts or the sump are full. However, simple on-off valves will probably still be needed at key points in the system to prevent water draining backwards theough the pipes when the pump(s) are idle.