WIMBORNE MODEL TOWN
DEVELOPMENT
RIVER SYSTEM: PHASE 4 DESIGN DOCUMENT
Issue 0.1
26th April 2017

This work is licensed under the Creative Commons Attribution-NonCommercial-ShareAlike 4.0 International License. To view a copy of this license, visit http://creativecommons.org/licenses/by-nc-sa/4.0/.

Annexes
A	Requirements Cross Reference
B	Hardware Identity
C	Software Identity
D	Spares
E	System Diagram – Automatic Water Controller
# INTRODUCTION
This document details the design of proposed enhancements to the Wimborne Model Town River System. The design has been created to meet the requirements contained in References 1 and 2 of Table 1 below and a Cross-reference between each requirement and the design elements that fulfil it is given in Annex A.
This issue of the document covers the requirements of Phase 4 of the work, as defined in Reference 2; the automation of the system. Phases 1 and 2 of the development are largely complete. Phase 3 is in progress and it is believed that a Design Document will not be needed to complete the work. When Phases 5 and 6 commence, an update to this document will be provided, if necessary.
The document provides a full description of the installed system to realise Phase 4 for use by future developers and maintainers.
Note:	It is a requirement of this Project that development shall be ‘agile’ in nature (Requirement 8.3 in Reference 1). What this means in practice is that elements of work from one phase may be brought forward or delayed as circumstances and funding dictate. This means that some of the work described in Phases 5 and 6 might be included in this Phase, should time and funding allow.
# RELATED DOCUMENTS
The following documents are related to this document.
Table 1: Related Documents
No	Requirement	Iss
1	WMT – Development – River System Requirements	0.5
2	WMT – Development – River System Phased Requirements	0.5
3	WMT – Development – River System Installation Specification	TBD
4	WMT – Development – River System User Manual	TBD

# DETAILED DESIGN
## Hardware
The full identification and quantities of all hardware items may be found in Annex B.
### Automated Control of the River System
#### System Controller
##### Raspberry Pi ?
Overall control of the system will be implemented using a Raspberry Pi ? (the Master Pi). This small single board computer has a 40 pin connector that carries 26 GPIO channels, plus power, 1-wire and an I2C bus. Additionally the device has four USB connectors, and one each of Ethernet, HDMI and power connectors. The device also has a Wireless and Bluetooth adaptor built in. This will not be needed for this project other than during development. A Micro SD Card slot is provided to carry the Operating System and program code.
The Master Pi will ????
During development, the Master Pi will be accessed via a monitor, mouse and keyboard and integrated with the system. Once integration is complete, the Master Pi will be run 'headless'.
The Master Pi will be housed in an equipment case installed ????.
#### Remote Sensors
Remote Sensors will include…..
##### Flow Sensors
…..
##### Level Sensors
…..
##### Other Sensors
….. ???????
#### Interfacing
##### 1-Wire ???
…...
##### Other Interfaces ???
…...
##### ?????

### Graphical User Interface
##### WMT Staff Interface
Web ???. This will allow:
- Monitoring of the running system (see Section 3.2.1.2).
- Manual override and control (see Section 3.2.2).
- ???
…..
##### Visitor Interface
Web ???. This will allow:
- Monitoring of the running system (see Section 3.2.1.2).
- ???
…..
#### Power Supplies
The following power supplies will be provided:
- Mains for pumps ????
- 12 V, 2.3A – ?????????
- 5 V, 2.5 A – Raspberry Pi. See Section3.1.1.2.2.
## Software
The full identification and quantities of all software items may be found in Annex B.
### Master Pi
#### Software Functions
##### Monitoring
Code will be written in Python and will implement the following functions:
- Monitor ????:
  - ????.
  - ???
The above functions will continue until a manual override is detected or the power is removed.
#### Control
Code will be written in Python and will implement the following functions:
Control ????:
- ????
- ????
### Remote Devices
#### Software Functions
##### Monitoring
Code will be written in Python and will implement the following functions:
- Monitor ???? and transmit results to the Master Pi:
  - ????.
  - ???
The above functions will continue until a manual override is detected or the power is removed.
#### Control
Code will be written in Python and will implement the following functions:
Control ???? when instructed by the Master Pi:
- ????
- ????
### Graphical User Interface
The Graphical User Interface will be implemented by running a webserver on the ??? The following standard software will be installed on the server:
- Webserver - nginx plus modules.
- DNS server -dnsmasq.
Server code will be written in HTML and Javascript and will implement the following functions:
- Provide ???? for the user to select:
  - Monitoring:
    - ?????:
      - ???.
  - Control:
    - For WMT Staff only, provide ???? for the user to select::
    - ?????:
      - ???.
  - ????
### Operating System
The Operating System used for the Master Pi will be Raspbian and ??? for the Remote Devices. During development, of both the Master Pi and the GUI, the Operating System will be run normally, but during deployment, the Master Pi and Remote Devices will be run in Read-only mode, to allow for uncontrolled shutdowns and restarts.
#### Software Documentation
Comments will be included in all software developed specifically for the WMT to allow future developers to maintain the code.
A full description of the implementation of code that provides the River System will be provided in the Installation Manual (see Reference 2 in Section 2).
## Environmental
All hardware will be contained within equipment cases.
The Master Pi will be installed within the ?????, so the environment is expected to be benign???. The equipment case will therefore function mainly to protect the equipment from unauthorised access.
The Remote Devices will be installed adjacent to where they are used. More attention will therefore be paid to the housing of this hardware, paying due attention to the need to keep the equipment cool and dry. This case will therefore include an internal heatsink to conduct heat from the air inside the case and therefore keep the internal environment below 35º C.
## Operational
### Powering Up and Down
The Operator will be able to:
- Start either of the systems by switching on the supply at the mains socket.
- Stop either of the systems by switching off the supply a the mains socket. This will be achieved safely by the methods defined in Sections 3.1.2.2.1 and 3.2.3.2.
## Reliability and Maintainability
### Reliability
- All components carrying powers in excess of 1 W will be derated by at least 20 % for power supplies and 50 % for other components.
- The SD Card will be protected from corruption by the methods defined in Sections 3.1.2.2.1 and 3.2.3.2.
- Adequate ventilation will be provided. It is not believed that forced cooling will be required, but if necessary, a fan will be incorporated to cool the components.
### Maintainability
- Full documentation will be provided as follows:
  - Design (this document).
  - Installation (to describe how to create the software and write it to the SD Card). See Reference 2 in Section 2.
  - User Manual showing the removal and replacement of components, where the procedure is not straightforward. See Reference 4 in Section 2.
- Spares will be provided as defined in Annex D.
- No special tools will be required to repair the system, other than standard items normally found in a general purpose tool kit.
- Full backups of all software developed will be provided.
- All software will be documented with comments.
## Safety
With the exception of the power supply inputs and ????, all circuits will operate at less than 20 V. The mains inputs to the PSUs and ??? will be contained within a protective case.
# ASSUMPTIONS
The following assumptions are made.
- Future system developers will have a working knowledge of Linux, Python programming and Web development.
- System maintainers will be sufficiently skilled in general maintenance to be able to follow the diagnostic instructions provided in the User Manual.

Annex A
Requirements Cross-Reference

Paragraph Numbers in Column 1 refer to Reference 1 in Section 2.
Functional
No	Requirement	Para

Operational
No	Requirement	Para

Environmental
No	Requirement	Para

Reliability
No	Requirement	Para

Maintainability
No	Requirement	Para

Safety
No	Requirement

Documentation
No	Requirement	Para

Miscellaneous
No	Requirement	Para

Annex B
Hardware Identity
This Annex defines the hardware required for system implementation. Many of these items are free delivery and some attract a delivery charge of a few pounds. Assume £10-15 total delivery. A list of spares may be found in Annex D. These would be procured at the same time as the Development items, so would attract no additional delivery costs.
River System Phase 4 Development
Computing Devices
Item	Identity	Qty	Cost Each	Total Cost
Master Computer	Raspberry Pi ??? (Raspberry Pi Foundation).	1	£30	£30

Interfaces and Accessories

Item	Identity	Qty	Cost Each	Total Cost

Power Supplies

Item	Identity	Qty	Cost Each	Total Cost

Miscellaneous

Item	Identity	Qty	Cost Each	Total Cost

Annex C
Software Identity
This Annex defines the software required for system implementation.
Item	Identity	Qty
Operating System	Raspbian for development and deployment .	2

Annex D
Spares
This Annex defines the spares required for system maintenance.
Item	Identity	Qty	Cost Each	Total Cost

Annex E - System Diagram: Automatic Water Controller

Add Drawing Here