WIMBORNE MODEL TOWN
DEVELOPMENT
RIVER SYSTEM: INSTALLATION SPECIFICATION
Issue 0.1
6th January 2019

This work is licensed under the Creative Commons Attribution-NonCommercial-ShareAlike 4.0 International License. To view a copy of this license, visit http://creativecommons.org/licenses/by-nc-sa/4.0/.

# INTRODUCTION
This specification provides information for future developers of the River Control System at Wimborne Model Town.
Where possible, the system has been designed to be as easy as possible to operate, maintain and upgrade.
This document should be read in conjunction with the Design Specification and the User Manual.
This document is split into two parts; the installation of the Bells hardware and software and the installation of the Webserver hardware and software.
## Development Documents
The following documents were generated as part of this development.
Table 1.1: Related Documents - Development
No	Document	Iss
1	Wimborne Model Town – River System - Requirements	?
2	Wimborne Model Town – River System - Design	?
3	Wimborne Model Town – River System – User Manual	?
4	Wimborne Model Town – River System – Software Design Specification	?

## Referenced Documents and Resources
The following documents and resources are useful for supporting development.
Table 1.2: Related Documents -River System Project

No	Resource	Ref
1	Python Tutorial	https://docs.python.org/2/tutorial/index.html
2	Python Documentation	https://docs.python.org/2/index.html
3	Raspberry Pi GPIO Tutorials	http://raspi.tv/
4	Python Lists	https://docs.python.org/2/glossary.html#term-list
5	Setting a static IP Address	https://www.modmypi.com/blog/how-to-give-your-raspberry-pi-a-static-ip-address-update
6	Readonly Root with OverlyFS	https://www.raspberrypi.org/forums/viewtopic.php?f=66&t=173063
7	How To Autorun A Python Script On Raspberry Pi Boot	Run as Another User
8	GitLab Project – River System	River System Project
9	Etcher – SD Card copier.	https://etcher.io/
10	Tutorial on backing up and restoring SD Cards.	http://thepihut.com/blogs/raspberry-pi-tutorials/17789160-backing-up-and-restoring-your-raspberry-pis-sd-card

# ABBREVIATIONS
- AP	-	Access Point
- ESD	-	Electrostatic Sensitive Device
- GPIO	-	General Purpose Input / Output
- IDE	-	Integrated Development Environment
- PCB	-	Printed Circuit Board
# PROJECT ARCHIVES
A copy of all project documentation, code and software environments may be found at the relevant GitLab Project, (see References 1.2.1.8 and 1.2.2.5).

# SYSTEM FUNCTIONS
## Hardware
### Installation
Installation of the hardware is covered in the User Manual and this document is confined to work that will only need to take place if the system has been revised and upgraded; an activity that might trigger a need to strip the system out or redesign some elements.
### Electrostatic Sensitive Devices
CAUTION	Electronic devices used in the system are sensitive to static electricity. Precautions should be taken when handling these devices in order to prevent permanent damage.
The Raspberry Pis and the other Printed Circuit Boards (PCBs) contain devices that can be damaged if they are exposed to static electricity. Static Electricity is readily generated when people walk over dry floors, rub against furniture or simply rub against their clothing. Although rarely noticed, the level generated is sufficient to damage devices if precautions are not taken. It is therefore recommended that no work be undertaken on these devices without taking one of the following actions:
1. If possible an ESD workstation be employed. An ESD workstation includes an Antistatic Mat, a conductive wrist band and a means of earthing the mat and band, usually via a three-pin mains plug with a resistive earth pin.
2. It is recognised that the WMT is not conducive to setting up an ESD workstation, so maintainers should endeavour to earth themselves by touching an earthed metal object at intervals during the work, especially after it has been necessary to leave the work area and return. A good compromise would be to use a wrist band clipped to a convenient earth point.
### Hardware Environment
The hardware in this system was developed and assembled before final debugging was carried out, since this proved to be the only feasible method in the time available. However, this is not essential, and a breadboard and local Ethernet could be employed for future enhancements.
### System Layout
Full details of the physical and electrical layout of the system may be found in the User Manual.
## Software
### Software Environment
Much of the development of the software for the River System Functions may be performed on any computing device, but will be simplified if suitable tools are available as detailed below. Debugging must be performed on the target device, with suitable hardware attached (see Section 4.1.3 above) in order that the Python Interpreter may import all the necessary libraries and the software functions may be observed in operation. During the original development Raspberry Pi Model Zeros running the Raspbian Operating System, were used for final development, with a Pi 3 being used for initial coding.
### Development Tools
Raspbian includes all of the tools necessary to write and develop the program. The original development was carried out using the IDLE Integrated Development Environment, but other development toolsets such as Thonny or Eclipse may be used if desired.
## Detailed Description Of Software Functions
A high-level description of the key features of the River System software is provided below. A detailed functional description of the software design may be found in the automatically generated documentation. The purpose of this is to allow future developers, who may not be experienced Python programmers, to understand how the more advanced features work.
Links to further research are also provided, where appropriate.
### General
The River System Functions code was written using Python Version 3.??. For simple code constructs and approaches, a good start would be this Python Tutorial. The full documentation for Python 3.x may be found in the Python Docs and may be needed to interpret the detailed descriptions provided below.
Similarly, the RPi.GPIO Library was used to control the input and output functions and a series of Tutorials may be found at Alex Eames site.
## Deployment
### Software Environment
The deployed image on the SD Card is the same as that used during development, except that the system is run in ‘read-only root’ mode. Details of how this may be done are given in the Raspberry Pi Forums entry Readonly Root with OverlyFS. This involves marking some areas of the system (such as the swap partition) as Read-only in fstab and also running a script to create a protected run-time environment.
### Network Configuration
In the final deployment there may be no DHCP server available, so each Pi has been given a static IP Address. Reference 1.2.5 provides a method of doing this on a Raspberry Pi and the following sections detail the procedure.
#### Set the Hostname
This may be done from within the Raspbian GUI by selecting ‘Raspberry Pi Configuration from the main Menu. Alternatively the hostname may be changed by typing:
sudo hostname SumpPi

etc, in a shell. Either way, a reboot will be required.
#### Setup a Static IP Address
To set a static IP address, enter a shell and type:
sudo nano /etc/dhcpcd.conf

At the bottom of the file add:
interface eth0
static ip_address=192.168.0.2/24
static routers=192.168.0.254
static domain_name_servers=192.168.0.1

Save the changes (Crtl O, <Enter>, Ctrl X).
A full list of assigned IP Addresses may be found in Reference 1.1.4 and the auto-generated software documentation, under ‘config.py’.
#### Enable SSH
SSH may be enabled in a number of ways, including from the GUI by using the ‘Raspberry Pi Configuration’ menu under ‘Preferences’. From the shell it may be enabled by simply creating a file called ‘SSH’ in /boot:
cd /boot
touch SSH
Raspbian will prompt the user to change the password after the next reboot, but it will accept the new password being identical to the old one.
### Change the Default User’s Password
The password may be changed in a number of ways, including from the GUI by using the ‘Raspberry Pi Configuration’ menu under ‘Preferences’. From the shell it may be changed by typing:
passwd

The terminal will prompt for the old password followed by Return and then the new password followed by Return . Finally the terminal will request that the new password be confirmed. Use:
Username: Pi
Password: river17

The IP addresses defined in Table 2 of Reference 1.1.4 should be used for the current deployment and the following login credentials should be used for all Pis:
Username: Pi
Password: river17
### Sump Pi Configuration
#### Time Synchronisation
The Master Pi, (currently SumpPi) has a physical Real Time Clock installed on GPIO Pins 1 to 6 rdate will be used on all Pi’s to synchronise all local clocks to the Real Time Clock installed in SumpPi. Configure Sump Pi to read and use this clock as detailed below:
Edit the file /boot/config.txt and add the following line:
dtoverlay=i2c-rtc,pcf2127

After restarting, the RasClock should be recognised and can be controlled with the hwclock command.
Edit the file /lib/udev/hwclock-set

Comment out or remove the three lines
if [ -e /run/sadaystemd/system ] ; then
    exit 0
fi

Comment out or remove the two lines which contain –systz
#### Autostart of the Sump Pi Software
After boot up, the relevant program is launched by including the following code in .bashrc for the Pi user:
if [ $(tty) == /dev/tty1 ]; then
cd rivercontrolsystem-master
./main.py
fi

Where <ID> is the identity of the Pi as given in Table 2 of Reference 1.1.4.
This will ensure that the program is only ever launched once and prevents subsequent logins via SSH from starting a new instance.
### Butts Pi(s) Configuration
#### Time Synchronisation
 To synchronise all local clocks to the Real Time Clock installed in SumpPi, install rdate on all Pis and on all clients synchronise the clock at startup using the following code in rc.local:
echo "Wait for master to start"
sleep 30

rdate -v 192.168.0.2
#### Autostart of the Butts Pi Software
This is achieved in a similar way to the Sump Pi configuration. Add the following lines at the bottom of the file home/pi/.bashrc:
if [ $(tty) == /dev/tty1 ]; then
cd rivercontrolsystem-master
./universal_monitor.py --id "ID"
fi

### Gate Pi(s) Configuration
Time SynchronisationTo synchronise all local clocks to the Real Time Clock installed in SumpPi, install rdate on all Pis and on all clients synchronise the clock at startup using the same code as for the other client Pis, as detailed above.
#### Autostart of the Gate Pi Software
This is achieved in a similar way to the Sump Pi configuration. Add the following lines at the bottom of the file home/pi/.bashrc:
if [ $(tty) == /dev/tty1 ]; then
cd rivercontrolsystem-master
./gate_valve.py --id "ID"
fi

# GENERAL MAINTENANCE ACTIVITIES
## Backing Up and Restoring SD Cards
There are several methods of backing up SD Cards. Two are described below:
### Backing Up
#### From Within Raspbian
Boot the system in the normal way, but interrupt execution of the minster_bells program by pressing CTRL-C several times. Start the Pixel Desktop by typing ‘startx’ at the prompt and pressing <RET>.
Once the desktop is running, insert a blank SD Card into a USB to SD Card adaptor and select Accessories – SD Card Copier from the main Menu. Follow the on-screen instructions.
Note:	This method can be a bit slow because the Pi has a relatively slow processor, which has to manage the copying at the same time as running the GUI.
#### From a Linux Computer
##### Identify the Device
In order to carry out this operation, it is necessary to identify the mounted SD Card. Insert the SD Card into a USB to SD Card adaptor, but do not plug it into the Linux machine yet.
Issue the following command in a shell:
df -h

Filesystem      Size  Used Avail Use% Mounted on
udev            3.9G     0  3.9G   0% /dev
tmpfs           794M  9.5M  785M   2% /run
/dev/sda1        58G   18G   38G  32% /
tmpfs           3.9G   38M  3.9G   1% /dev/shm
tmpfs           5.0M  4.0K  5.0M   1% /run/lock
tmpfs           3.9G     0  3.9G   0% /sys/fs/cgroup
/dev/sdb1       286G  160G  112G  59% /home
tmpfs           794M   36K  794M   1% /run/user/1000
Insert the SD Card into a USB slot and re-issue the df command.
df -h

Filesystem      Size  Used Avail Use% Mounted on
udev            3.9G     0  3.9G   0% /dev
tmpfs           794M  9.5M  785M   2% /run
/dev/sda1        58G   18G   38G  32% /
tmpfs           3.9G   38M  3.9G   1% /dev/shm
tmpfs           5.0M  4.0K  5.0M   1% /run/lock
tmpfs           3.9G     0  3.9G   0% /sys/fs/cgroup
/dev/sdb1       286G  160G  112G  59% /home
tmpfs           794M   36K  794M   1% /run/user/1000
/dev/sdc2       6.8G  5.4G  1.1G  84% /media/terry/7f593562-9f68-4bb9-a7c9-2b70ad620873
/dev/sdc1        63M   21M   43M  34% /media/terry/boot
Two new devices are now visible sdc1 and sdc2. These are the two partitions on the Raspbian SD Card; it is the device that is of interest (eg, sdc) not the full partition name.
##### Writing an Image
To backup up an SD Card in Linux, issue the following commands in a shell to backup an SD card:
  sudo dd if=/dev/sdc of=~/SDCardBackup.img

Note1:	The source of the backup, (in the example sdc) should be changed to suit the Linux installation in use.
Note2:	The destination may be anywhere on the Linux installation and it is suggested that the filename reflects the contents and the date of the backup.
Note 3:	The dd command does not show any feedback so wait until the command prompt re-appears.
### Restoring
#### Using Etcher
Etcher is a cross-platform graphical SD Card writing tool which takes much of the complexity out of writing an image to an SD Card. The tool may be downloaded from the Etcher Website.
#### From a Linux Computer
After establishing the identity of the device it needs be unmounted. However, this must be done partition by partition by using the partition number as well. Issue the following commands for each partition:
sudo umount /dev/sdc1
sudo umount /dev/sdc2

etc….

Write the original image to the SD Card:
sudo dd bs=4M if=~/SDCardBackup.img of=/dev/sdc

Note1:	The bs=4M option sets the 'block size' on the SD card to 4Meg. If you get any warnings, then change this to 1M instead, but that will take a little longer to write.
Note2:	Wait until the command completes because ‘dd’ provides no feedback on progress.

Before ejecting the SD card, ensure that the Linux machine has completed writing to it by issuing the command:
sudo sync

See The Pi Hut for more information, including details of how to backup and restore SD cards on Windows or a Macintosh.