WIMBORNE MODEL TOWN
RIVER SYSTEM
USER AND MAINTENANCE MANUAL
Issue 0.1
12th July 2020

This work is licensed under the Creative Commons Attribution-NonCommercial-ShareAlike 4.0 International License. To view a copy of this license, visit http://creativecommons.org/licenses/by-nc-sa/4.0/.

# INTRODUCTION
This manual provides information for staff and maintainers of the River System Hardware and Software at Wimborne Model Town. These features were added during the period 2017 to 2020. There is still a considerable amount of work to be completed, but the detailed design work is now well advanced and the remaining effort will mostly be confined to the construction, installation and setting to work of the various devices that comprise the system.
It also covers the (possibly temporary) VPN Server added in July 2020.
Where possible, the system has been designed to be as easy as possible to operate, maintain and upgrade.
If future upgrades to the system are required, then developers should read the Installation Specification in conjunction with this document.
# RELATED DOCUMENTS
The following documents are related to this document.
Table 2.1: Related Documents

No	Requirement	Iss
1	Wimborne Model Town – River System - Requirements	0.5
2	Wimborne Model Town – River System – Software Requirements	0.2
3	Wimborne Model Town – River System - Design	0.5
4	Wimborne Model Town – River System – Software Design	0.9
5	Wimborne Model Town – River System – Installation Specification	0.11
6.	Wimborne Model Town – River System – Project Archive	https://gitlab.com/wmtprojectsteam/rivercontrolsystem
7	WMT – River System – Sensor & Control Assy – Composite Document	0.7
8	WMT – River System – Gate Valve Assy – Composite Document	0.8

# ABBREVIATIONS
- ESD	-	Electrostatic Sensitive Device
- GUI	-	Graphical User Interface
- LHS	-	Left Hand Side
- PSU	-	Power Supply Unit
- RHS	-	Right Hand Side
- SAC	-	Sensor and Control Assembly
- SSH	-	Secure Shell
- USB	-	Universal Serial Bus
- VPN	-	Virtual Private Network
- WMT	-	Wimborne Model Town

# OPERATING INSTRUCTIONS
## Routine Operations
### Daily
There no daily operations required for the River System other than a visual inspection of the level and flow of water in the river. Any unusual circumstances should be investigated to prevent the possible loss of water from the system.
### Backing Up of Data
??????????? How will we do this ?????????????????????

???????????????? TBD ?????????????????????
## System Control
### Startup
At present there is no overall system control and individual devices are simply switched on at the nearest mains supply socket. These are:
- Sump SAC – Inside the Green Box.
- Wendy Street SAC – Beneath the adjacent ramp.
- Stage SAC – Behind the Stage.
- Lady Hanham SAC – Behind the Lady Hanham Building.
- Gazebo SAC (when fitted) – Beneath the eaves at the rear of the Gazebo
- NAS Box – Inside Railway Room Store.
- Wendy Butts Gate Valve - Beneath the adjacent ramp.
- Stage Butts Gate Valve - Beneath the adjacent ramp.
- Matrix Pump Gate Valves - Wendy Butts Gate Valve - Beneath the adjacent ramp.
- Lady Hanham Gate Valves – Behind the Lady Hanham Building.
- Gazebo Gate Valve (when fitted) – Beneath the eaves at the rear of the Gazebo
Note:	From the above it can be seen that some mains outlets supply more than one device (eg Beneath the ramp in the Wendy Street area).
### Shutdown
Apart from the NAS Box, all devices should be shut down properly before power is removed. This is achieved by logging into the device using SSH and issuing the following command:
sudo poweroff
Usernames and passwords for all River System devices, plus the Web and VPN Servers are held in the safe. Login is therefore possible by connecting to the River System Network by connecting to the ‘WMT-Guest’ WiFi (see Section ???? below) or by using the VPN facility to login remotely.
Note:	Hostnames or IP addresses will be needed in order to login in to the River System devices. The command to use SSH takes the form:
ssh <username>@<hostname or IP Address>
eg:
ssh pi@192.168.0.2
Notes:
1.	Before removing the mains supply, as detailed in Section 4.2.2 above, ensure that all devices that derive their power from that socket have been properly shut down. For Gate Valves it may be possible to remove the 12 V DC supply at the input to the device (see Section ???? below)
2.	In due course there will be a Staff and Visitor GUI provided on site. The main purpose of this GUI will be allow monitoring of the water levels, etc within the River system, but a certain amount of control will also be available for staff only, including a remote shutdown of the devices in the system.
## Isolating the System
If desired, for maintenance or during the winter closed period, the system may be shut down completely by turning off the mains power switches adjacent to each device. To power up, the mains switch should be set to on.
### In the Case of a Fault
Should a fault occur with the system, removing the 3-pin plug from the mains socket will completely isolate the associated device.

# MAINTENANCE INSTRUCTIONS
## Electrostatic Sensitive Devices
CAUTION	Electronic devices used in the system are sensitive to static electricity. Precautions should be taken when handling these devices in order to prevent permanent damage.
The Raspberry Pis, the UPS Pico and the MOSFET Driver all contain devices that could be damaged if they are exposed to static electricity. Static Electricity is readily generated when people walk over dry floors, rub against furniture or simply rub against their clothing. Although rarely noticed, the level generated is sufficient to damage devices if precautions are not taken. It is therefore recommended that no work be undertaken on these devices without taking one of the following actions:
1. If possible an ESD workstation be employed. An ESD workstation includes an Antistatic Mat, a conductive wrist band and a means of earthing the mat and band, usually via a three-pin mains plug with a resistive earth pin.
2. It is recognised that the WMT is not conducive to setting up an ESD workstation, so maintainers should endeavour to earth themselves by touching an earthed metal object at intervals during the work, especially after it has been necessary to leave the work area and return. A good compromise would be to use a wrist band clipped to a convenient earth point.
## System Diagrams
Illustrations ????? below show the electrical and electronic circuits that comprise the River System. The originals of these drawings may be found on the Development Server at the Project Archive (see Section ??????).
Illustration 5.1: Overall System Diagram – Sheet 1

## Illustration 5.2: Overall System Diagram – Sheet 2

Illustration 5.3: Overall System Diagram – Sheet 3

## Illustration 5.4: Overall System Diagram – Sheet 4

## System Layout – General Arrangement
### TBD
## Spares
The following spare items have been purchased to allow maintenance of the system.
Table 5.1: River System Spares

## System Wiring

## Diagnosing a Fault
#### Connecting a Keyboard, Mouse and Monitor to the Pi
To gain directaccess to any Pi, ???.
Further information regarding the Raspberry Pi and how to use it may be found on the Internet at https://www.raspberrypi.org/.
#### Sensor and Control Assy
?????
#### Gate Valve
?????

## Removal and Replacement Instructions
### SAC
The following Sections provided detailed procedures for removing and replacing the spares listed in Section 4.3 above.
Warning:	Great care should be exercised when measuring signals or removing or replacing items within the Minster Bells Control Box. All precautions outlined in Section 5.1 and this Section should be observed to ensure that no damage to the equipment is inadvertently caused.
#### Opening the IP65 Box
??????.
#### Real Time Clock (RTC) Module
??????
#### PSU for the Pi
Replacement of the Pi PSU is relatively straightforward.
1. Unplug the PSU from the mains socket.
2. Swing back the lid of the Control Box (Section 5.7.1.1).
3. Remove the micro-USB connector from its socket on the Pi.
4. Withdraw the barrel connector through the access
Replacement is the reverse of the above.
#### Pi Micro SD Cards
Replacement of the Micro SD Card is relatively straightforward.
1. Swing back the lid of the Control Box and remove the electronics assembly (Sections 5.7.1.1 and 5.7.1.2).
2. Carefully remove the SD card from the left hand side of the Pi.
Note:	The SD Card is installed underneath the Pi with the contacts uppermost.
Replacement is the reverse of the above.
### Webserver
The following Sections provided detailed procedures for removing and replacing the spares listed in Section 5.4 above.
Warning:	Great care should be exercised when removing or replacing items within the Webserver equipment case. All precautions outlined in Section 5.1 and this Section should be observed to ensure that no damage to the equipment is inadvertently caused.
#### Opening the Main Equipment Case
Access to the components housed inside the equipment case may be achieved by unclipping the lid and removing it (refer to Illustrations 5.5.6 and 5.7).
#### Withdrawing the Main Electronics Mounting Board
?????.
#### Replacement of the Ethernet Adaptor
Replacement of the Ethernet Adaptor is very straightforward.
Disconnect the Adaptor from the USB extension lead and the Ethernet drop cable.
Replacement is the reverse of the above.
#### Opening the Gazebo Equipment Case
Access to the components housed inside the equipment case may be achieved by unscrewing the four lid reataing screws and removing it (refer to Illustration 5.8).