Wimborne Model Town River System Graphical User interface

A graphical display is required to show visitors to Wimborne Model Town information about the River System.

The display must be informative and intuitive providing the visitor with an appreciation of the workings and status of the river system without overwhelming them with technical detail.

Raw data on the status of the river system is obtained from probes that interface to a federated computer system (Raspberry Pis) that automatically controls pumps and valves to maintain the river water level within predefined bounds.

The raw data is collected in and made available to the computer system, including the graphical display, from a database. Information derived from this data will be shown on the graphical display as animated icons overlaid on a map of the Model Town

As part of the graphical display project what we need from the students of Canford School are:

- An attractive, simplified and stylised map of the river and water storage system.
- Animated icons plus numerical valve for the quantity being displayed. More than one icon of any one type is required on the map.

Icon[1]	Measured quantity range	Measured quantity units	Comment
Water flow direction and rate	Forward / reverse / 0 to 100%	Litres per second / Units need to be scalable	Maximum flow rate depends on location of probe to S/W need to accommodate this
Water level	0 to 1000 mm	Litres[2] / Units need to be scalable	Maximum water level depends on location of probe to S/W need to accommodate this
Water valve status	Fully closed to fully open	25% steps	The Valves can actually do increments of 1%.
Pump speed	Off to fully on	10% steps
Max/min float switch	3 states Max / Intermediate/Min
Amount of water in river system	0 to 20,000 litres	Litres / Units need to be scalable	I assume this will be calculated elsewhere and read from the database.
Amount of water in storage	0 to 10,000 litres	Litres / Units need to be scalable	Ditto
[1] The icon need to give the viewer a cue on what is being displayed and the status of that data.
[2] Water level is measured by probes capable of measuring from 0mm to 1000mm in 25mm steps, the probes are inserted in containers of varying sizes. The calculation of the number of litres in each container will be carried out elsewhere and stored in the database.

As detailed in the full Requirement Specification (WMT_River_System_GUI_Reqs_Iss_1.0), the features described above is required to be presented as a web site served to users from a pre-existing Webserver at the Wimborne Model Town.

In order to maximise maintainability, the software to provide the data to be displayed with the animated icons is required to be written using the Flask micro-framework which uses the Python Programming language to retrieve and process the data.