WIMBORNE MODEL TOWN
DEVELOPMENT
RIVER SYSTEM: INSTALLATION SPECIFICATION
Issue 0.2
14th May 2019

This work is licensed under the Creative Commons Attribution-NonCommercial-ShareAlike 4.0 International License. To view a copy of this license, visit http://creativecommons.org/licenses/by-nc-sa/4.0/.

# INTRODUCTION
This specification provides information for future developers of the River Control System at Wimborne Model Town.
Where possible, the system has been designed to be as easy as possible to operate, maintain and upgrade.
This document should be read in conjunction with the Design Specification and the User Manual.
## Development Documents
The following documents were generated as part of this development.
Table 1.1: Related Documents - Development
No	Document	Iss
1	Wimborne Model Town – River System - Requirements	?
2	Wimborne Model Town – River System - Design	?
3	Wimborne Model Town – River System – User Manual	?
4	Wimborne Model Town – River System – Software Design Specification	?

## Referenced Documents and Resources
The following documents and resources are useful for supporting development.
Table 1.2: Related Documents -River System Project

No	Resource	Ref
1	Python Tutorial	https://docs.python.org/3.7/tutorial/index.html
2	Python Documentation	https://docs.python.org/3.7/index.html
3	Raspberry Pi GPIO Tutorials	http://raspi.tv/
4	Deleted
5	Setting a static IP Address	https://www.modmypi.com/blog/how-to-give-your-raspberry-pi-a-static-ip-address-update
6	Make the SD CardReadonly	https://learn.adafruit.com/read-only-raspberry-pi/
7	How To Autorun A Python Script On Raspberry Pi Boot	Run as Another User
8	GitLab Project – River System	River System Project
9	Etcher – SD Card copier.	https://etcher.io/
10	Tutorial on backing up and restoring SD Cards.	http://thepihut.com/blogs/raspberry-pi-tutorials/17789160-backing-up-and-restoring-your-raspberry-pis-sd-card
11	Tutorial on shrinking image files.	https://softwarebakery.com//shrinking-images-on-linux

# ABBREVIATIONS
- AP	-	Access Point
- ESD	-	Electrostatic Sensitive Device
- GPIO	-	General Purpose Input / Output
- IDE	-	Integrated Development Environment
- PCB	-	Printed Circuit Board
# PROJECT ARCHIVES
A copy of all project documentation, code and software environments may be found at the relevant GitLab Project, (see References 1.2.1.8).

# SYSTEM FUNCTIONS
## Hardware
### Installation
Installation of the hardware is covered in the User Manual and this document is confined to work that will only need to take place if the system has been revised and upgraded; an activity that might trigger a need to strip the system out or redesign some elements.
### Electrostatic Sensitive Devices
CAUTION	Electronic devices used in the system are sensitive to static electricity. Precautions should be taken when handling these devices in order to prevent permanent damage.
The Raspberry Pis and the other Printed Circuit Boards (PCBs) contain devices that can be damaged if they are exposed to static electricity. Static Electricity is readily generated when people walk over dry floors, rub against furniture or simply rub against their clothing. Although rarely noticed, the level generated is sufficient to damage devices if precautions are not taken. It is therefore recommended that no work be undertaken on these devices without taking one of the following actions:
1. If possible an ESD workstation be employed. An ESD workstation includes an Antistatic Mat, a conductive wrist band and a means of earthing the mat and band, usually via a three-pin mains plug with a resistive earth pin.
2. It is recognised that the WMT is not conducive to setting up an ESD workstation, so maintainers should endeavour to earth themselves by touching an earthed metal object at intervals during the work, especially after it has been necessary to leave the work area and return. A good compromise would be to use a wrist band clipped to a convenient earth point.
### Hardware Environment
The hardware in this system was developed and assembled before final debugging was carried out, since this proved to be the only feasible method in the time available. However, this is not essential, and a breadboard and local Ethernet could be employed for future enhancements.
### System Layout
Full details of the physical and electrical layout of the system may be found in the User Manual.

## Software
### Software Environment
Much of the development of the software for the River System Functions may be performed on any computing device, but will be simplified if suitable tools are available as detailed below. Debugging must be performed on the target device, with suitable hardware attached (see Section 4.1.3 above) in order that the Python Interpreter may import all the necessary libraries and the software functions may be observed in operation. During the original development Raspberry Pi Model Zeros, running the Raspbian Operating System, were used for final development, with a Pi 3 being used for initial coding.
### Development Tools
Raspbian includes all of the tools necessary to write and develop the program. Much of the original development was carried out using the IDLE Integrated Development Environment, but other development toolsets such as Thonny or Eclipse may be used if desired.
## Detailed Description Of Software Functions
A detailed functional description of the River System software design may be found in the automatically generated documentation.
### General
The River System Functions code was written using Python Version 3.7.x. For simple code constructs and approaches, a good start would be the Python Tutorial at Reference 1.2.1. The full documentation for Python 3.x may be found in the Python Docs at Reference 1.2.2 and may be needed to interpret the detailed descriptions provided below.
Similarly, the RPi.GPIO Library was used to control the input and output functions and a series of Tutorials may be found at Alex Eames site (Reference 1.2.3).
## Deployment
### Software Environment
The deployed image on the SD Card is Raspbian Lite, run in ‘read-only root’ mode. Details of how to prepare the SD Card for deployment are given below. The Initial Setup stage is easiest to perform if a separate PC is used.
#### Prepare the Basic Installation
Download the appropriate version of Raspbian Lite from https://www.raspberrypi.org/downloads/raspbian/ and unzip the image using the host PC’s native tool. Burn the image file to an 8 GB SD Card (using an appropriate adaptor) as described in Section 5 below. Remove the SD Card from the PC.
#### Initial Setup
Insert the SD Card into a Raspberry Pi computer and apply power.
Note:	Any Raspberry Pi will do for this and many of the the subsequent steps, but access to the Internet will be needed and it is less likely that issues will subsequently be encountered if a Raspberry Pi Zero is used.
After the system has booted, log in using the Username ‘Pi’ and the password ‘raspberry’.
Type the following at the command line:
sudo raspi-config

Using raspi-config’s menu items setup the following:
1. Change the password to ‘river17’.
2. If a plugin WiFi adaptor is being used during this process, then enter ‘Network Options’ and setup the SSID and Passphrase.
3. Enter ‘Boot Options’ and set the Pi to boot into the CLI and automatically log in to the Pi User.
4. Under ‘Localisation Options’, check that:
  1. The ‘Locale’ and ‘Keyboard’ settings match the keyboard type that is intended to be used for the River System setup.
  2. If a plugin WiFi adaptor is being used during this process, then setup the WiFi Channel.
  3. In the ‘Timezone’ setting, select ‘UTC’.
5. Under Interfacing Options’, enable ‘SSH’ and ‘I2C’.
6. Select ‘Finish’ and ‘Reboot’.
Note:	Do NOT expand the SD Card at this stage.
#### Common Software Installation
Use the following command to install the additional Python modules needed for execution of the Software Framework:
sudo apt-get update
sudo apt-get upgrade
sudo apt-get install rdate
sudo apt-get install RPi.GPIO
sudo apt-get install python3
sudo apt-get install python3-pip
pip3 install adafruit-circuitpython-ads1x15

Shutdown the Pi:
sudo shutdown now

Remove power from the Pi and remove the SD Card.
Backup the SD Card, as described in Section 5.1, giving the image file the name:
YYYY-MM-DD_River_System_Base_SD-Card.img

This ‘Base’ image subsequently be used to create SD Card for specific Pis.
### Prepare SD Cards for Specific Pis
For this this point onwards, it is assumed that all the preceding steps in Section 4.4.1 above have been carried out or that the SD Card image created at an earlier time has been used to create the new SD Card.
#### Expand the SD Card
Type the following at the command line:
sudo raspi-config

Using raspi-config’s menu items setup the following:
Under ‘Advanced Options’, expand the SD Card.
#### 4.4.1.4 Additional Network Configuration
#### In the final deployment there may be no DHCP server available, so each Pi has been given a static IP Address. Reference 1.2.5 provides a method of doing this on a Raspberry Pi and the following sections detail the procedure.
#### 4.4.1.4.1 Setup a Static IP Address
#### To set a static IP address, enter a shell and type:
sudo nano /etc/dhcpcd.conf
#### At the bottom of the file add:
interface eth0
static ip_address=192.168.0.2/24
static routers=192.168.0.254
static domain_name_servers=192.168.0.1
#### Save the changes (Crtl O, <Enter>, Ctrl X).
#### Note: In the example above, the allocated IP Address applies to sumppi. Remote Pis will have their static IP Address updated during the specific configurations described below.
#### Update the Static IP Address
Using the procedure given in Section 4.4.1 above, update the Pi’s IP Address to match the device being configured.
A full list of assigned IP Addresses may be found in Reference 1.1.4 and the auto-generated software documentation, under ‘config.py’.
#### Adding the Software Framework
On a suitable PC and copy the latest version of the Software Framework from the WMT repository at https://gitlab.com/wmtprojectsteam/rivercontrolsystem/tree/master. This may be done in a number of ways and if the git repository is already installed on the PC, and up to date with the referenced repository, then the ‘rivercontrolsystem‘ directory may be copied directly to the ‘pi’ directory on the SD Card (plugged into an adaptor). Alternatively, the code may be downloaded from the referenced site, unzipped and copied in the same way.
##### Making the SD Card Read-Only
This procedure is not reversible, and will prevent the Readings and Log files being written to the SD Card, so should only be carried out when a strategy for storing this information has been agreed and implemented. Setting the SD Card to Read-Only mode may be done using the procedure in the following web page https://learn.adafruit.com/read-only-raspberry-pi/. This involves running a script to create a protected run-time environment.

### Additional Sump Pi Configuration
#### Setting the Hostname
Run ‘raspi-config’, enter ‘Network Options’, and set the hostname to ‘sumppi’.
#### Time Synchronisation
The Master Pi, (currently sumppi) has a physical Real Time Clock installed on GPIO Pins 1 to 6 rdate will be used on all Pi’s to synchronise all local clocks to the Real Time Clock installed in sumppi. Configure Sump Pi to read and use this clock as detailed below:
Edit the file /boot/config.txt and add the following line:
dtoverlay=i2c-rtc,pcf2127

After restarting, the RasClock should be recognised and can be controlled with the hwclock command.
Edit the file /lib/udev/hwclock-set
Comment out or remove the three lines
if [ -e /run/sadaystemd/system ] ; then
    exit 0
fi

Comment out or remove the two lines which contain –systz
#### Installation and Configuration of Software Specific to SumpPi
In a shell issue the following command:
sudo apt-get install xinetd
sudo nano etc/xinetd.d/time

In two places, change ‘disabled=yes’ to ‘disabled=no’
#### Autostart of the Sump Pi Software
After boot up, the relevant program is launched by including the following code in .bashrc for the Pi user:
if [ $(tty) == /dev/tty1 ]; then
cd rivercontrolsystem
./main.py
fi

Where <ID> is the identity of the Pi as given in Table 2 of Reference 1.1.4.
This will ensure that the program is only ever launched once and prevents subsequent logins via SSH from starting a new instance.

### Butts Pi(s) Configuration
#### Time Synchronisation
 To synchronise the local clock to the Real Time Clock installed in sumppi, use the following code in rc.local:
echo "Wait for master to start"
sleep 30

rdate -v 192.168.0.2
#### Autostart of the Butts Pi Software
This is achieved in a similar way to the Sump Pi configuration. Add the following lines at the bottom of the file home/pi/.bashrc:
if [ $(tty) == /dev/tty1 ]; then
cd rivercontrolsystem
./universal_monitor.py --id "ID"
fi

Where ‘ID’ is the Device Name as detailed in Reference 1.1.4.
### Gate Pi(s) Configuration
#### Time Synchronisation
To synchronise the local clock to the Real Time Clock installed in sumppi, use the same code as for the other client Pis, as detailed above.
#### Autostart of the Gate Pi Software
This is achieved in a similar way to the Sump Pi configuration. Add the following lines at the bottom of the file home/pi/.bashrc:
if [ $(tty) == /dev/tty1 ]; then
cd rivercontrolsystem
./gate_valve.py --id "ID"
fi

Where ‘ID’ is the Device Name as detailed in Reference 1.1.4.
# GENERAL MAINTENANCE ACTIVITIES
## Backing Up and Restoring SD Cards
There are several methods of backing up SD Cards. Two are described below:
### Backing Up
#### From Within Raspbian
Boot the system in the normal way, but interrupt execution of the minster_bells program by pressing CTRL-C several times. Start the Pixel Desktop by typing ‘startx’ at the prompt and pressing <RET>.
Once the desktop is running, insert a blank SD Card into a USB to SD Card adaptor and select Accessories – SD Card Copier from the main Menu. Follow the on-screen instructions.
Note:	This method can be a bit slow because the Pi has a relatively slow processor, which has to manage the copying at the same time as running the GUI.
#### From a Linux Computer
##### Identify the Device
In order to carry out this operation, it is necessary to identify the mounted SD Card. Insert the SD Card into a USB to SD Card adaptor, but do not plug it into the Linux machine yet.
Issue the following command in a shell:
df -h

Filesystem      Size  Used Avail Use% Mounted on
udev            3.9G     0  3.9G   0% /dev
tmpfs           794M  9.5M  785M   2% /run
/dev/sda1        58G   18G   38G  32% /
tmpfs           3.9G   38M  3.9G   1% /dev/shm
tmpfs           5.0M  4.0K  5.0M   1% /run/lock
tmpfs           3.9G     0  3.9G   0% /sys/fs/cgroup
/dev/sdb1       286G  160G  112G  59% /home
tmpfs           794M   36K  794M   1% /run/user/1000
Insert the SD Card into a USB slot and re-issue the df command.
df -h

Filesystem      Size  Used Avail Use% Mounted on
udev            3.9G     0  3.9G   0% /dev
tmpfs           794M  9.5M  785M   2% /run
/dev/sda1        58G   18G   38G  32% /
tmpfs           3.9G   38M  3.9G   1% /dev/shm
tmpfs           5.0M  4.0K  5.0M   1% /run/lock
tmpfs           3.9G     0  3.9G   0% /sys/fs/cgroup
/dev/sdb1       286G  160G  112G  59% /home
tmpfs           794M   36K  794M   1% /run/user/1000
/dev/sdc2       6.8G  5.4G  1.1G  84% /media/terry/7f593562-9f68-4bb9-a7c9-2b70ad620873
/dev/sdc1        63M   21M   43M  34% /media/terry/boot
Two new devices are now visible sdc1 and sdc2. These are the two partitions on the Raspbian SD Card; it is the device that is of interest (eg, sdc) not the full partition name.
##### Writing an Image
To backup up an SD Card in Linux, issue the following commands in a shell to backup an SD card:
  sudo dd if=/dev/sdc of=~/SDCardBackup.img

Note1:	The source of the backup, (in the example sdc) should be changed to suit the Linux installation in use.
Note2:	The destination may be anywhere on the Linux installation and it is suggested that the filename reflects the contents and the date of the backup.
Note 3:	The dd command does not show any feedback so wait until the command prompt re-appears.
Note 4:	After the backup is completed, the image may be compressed if desired, using the ‘zip’ utility. (This is not installed by default on many Linux systems.) Compress the image using the following command:
zip SDCardBackup.zip SDCardBackup.img

Where the filename of the zipped up file and the original image reflect the date and content of the image, eg: zip 2019-05-01_V4_Gate_Valve_Backup.zip 2019-05-01_V4_Gate_Valve_Backup.img.
### Restoring
There are several ways to restore an image that was previously backed-up.
Note:	If the original image has been expanded within Raspbian, it is likely that it will not fit onto the SD Card. Images may be shrunk using the procedure detailed on Reference 1.2.11.
#### Using Etcher
Etcher is a cross-platform graphical SD Card writing tool which takes much of the complexity out of writing an image to an SD Card. The tool may be downloaded from the Etcher Website.
#### From a Linux Computer
After establishing the identity of the device it needs be unmounted. However, this must be done partition by partition by using the partition number as well. Issue the following commands for each partition:
sudo umount /dev/sdc1
sudo umount /dev/sdc2

etc….

Write the original image to the SD Card:
sudo dd bs=4M if=~/SDCardBackup.img of=/dev/sdc

Note1:	The bs=4M option sets the 'block size' on the SD card to 4Meg. If you get any warnings, then change this to 1M instead, but that will take a little longer to write.
Note2:	Wait until the command completes because ‘dd’ provides no feedback on progress.

Before ejecting the SD card, ensure that the Linux machine has completed writing to it by issuing the command:
sudo sync

See The Pi Hut for more information, including details of how to backup and restore SD cards on Windows or a Macintosh.