WMT RIVER SYSTEM
Options for A/D Converters for Use with the Rapberry Pi
# INTRODUCTION
Unlike the Arduino, the Raspberry Pi does not come with an Analogue to Digital Converter. It has up to 26 GPIO channels, some of which can be utilised for serial buses, but if conversion from analogue values is required, some form of external A/D Converter is needed.
This document compares the options for adding this functionality in the context of the River System. It includes the methods by which the devices would be interfaced to the Pi.
# SUMMARY OF OPTIONS AVAILABLE
The following is a list of the readily available options:
- 8 to 12 Bit Integrated Circuit, parallel data output – DIL Package
- 8 to 12 Bit Integrated Circuit, serial data output – DIL Package
- 8 to 12 Bit Integrated Circuit – Surface Mount Package
- Pre-packaged 8 to 12 Bit Module.

Each of these options is described in detail below.
# CONSTRAINTS SPECIFIC TO THE RIVER SYSTEM
It has already been decided that the River System hardware will be based around the Raspberry Pi. Amongst other factors, cost and versatility drove this decision.
None of the applications for the River System require a fast A/D, so this parameter has not been specifically considered. There are devices available which are extremely slow (eg 10 sps), but they tend to be more expensive and would suffice anyway. The cheapest devices have a sample rate of at least 20 ksps.
# DETAILED DESCRIPTION OF THE VARIOUS OPTIONS
## 8 to 12 Bit IC, Parallel Data Output – DIL Package
These devices are becoming increasingly rare due to the prevalence of surface mount and serial interfaces. A brief search on the RS Components website revealed 43 products starting at £3.36 plus VAT to over £60 each. A 12 bit device is available for about £9.50 with other resolutions costing comparatively less.
The only real benefit of using this type of device is that, being a DIL packaged device, it is easy to build into prototypes using Veroboard. It can be simple to interface this device to a Pi if sufficient GPIO pins are available, but even an 8-bit device would use nearly a third of the available pins. If the Pi in question was only being used to read this analogue level and up to one Magnetic Level Sensor (say), then this could be a relatively cheap approach. However, the chip would have to be assembled onto some kind of PCB (or Veroboard) with associated power supply smoothing, so the overall cost would probably be about £5 to £10 on Veroboard or considerably more on a dedicated PCB.
If it is required that more sensors routed to a given Pi, then a Bus Expander would be needed, such as the MCP23017 which costs around £1 plus VAT. However if all of the additional sensors were analogue, then devices with analogue multiplexers built in are available starting at around £5.75.
## 8 to 12 Bit IC, Serial Data Output – DIL Package
These devices are less rare than their parallel counterparts but there are still rarer than surface mount types. A brief search on the RS Components website revealed 55 products starting at £2.31 plus VAT to around £9 each. The only 12 bit device was actually cheaper than the more expensive 10 bit types, at about £3.30 with other resolutions costing comparatively less.
As with the parallel types, devices with analogue multiplexers built in are available starting at around £2.75.
Many of the devices found on the RS Components website provided an SPI serial interface, although I2C types are also available. The Raspberry Pi can interface to both of these bus types, although raw support for I2C in Python seems poor compared to SPI.
The use of the Serial bus topology would simplify interface board design, but would still require the addition of circuit board and smoothing amongst other things.
## 8 to 12 Bit IC, Serial Data Output – Surface Mount Package
These devices are less rare than their DIL counterparts. A brief search on the RS Components website revealed over 200 products starting at £0.94 plus VAT (for 2-off) to around £50 each.
As with the two DIL types, devices with analogue multiplexers built in are available starting at around £4.
Many of the devices found on the RS Components website provided an SPI serial interface, although I2C types are also available.
Surface Mount packages do not lend themselves to prototyping on Veroboard and are more difficult to solder, adding to the cost of production, which would probably more than discount the costs saved because the devices are cheaper than their DIL counterparts.
## Pre-packaged 8 to 12 Bit Module
The problems associated with building the devices into some form of circuit board would be obviated by buying a pre-packaged module. A number of specialist suppliers cater for the raspberry Pi (and Arduino) market and the bigger suppliers also provide Tutorials and Python Modules to make integration of the hardware simpler.
The following is a description of many of the currently available types.
## ADC Pi
This is an 8 channel 17 bit converter which communicates with the Pi via the I2C bus. It has the following specification:
- 8 x 17-bit 0 to 5V Single Ended Inputs
- Control via the Raspberry Pi I2C port
- Stack up to 4 ADC Pi boards on a single Raspberry Pi
- Jumper selectable I2C addresses
- Buffered 5V I2C port
- Based on the MCP3424 from Microchip Technologies Inc
- Single Ended full-scale range of 5.0V
- On-board 2.048V reference voltage (Accuracy ± 0.05%, Drift: 15 ppm/°C)
- On-Board Programmable Gain Amplifier (PGA): Gains of 1, 2, 4 or 8
- Programmable Data Rate Options:
      - 3.75 SPS (17 bits)
      - 15 SPS (15 bits)
      - 60 SPS (13 bits)
      - 240 SPS (11 bits)
- One-Shot or Continuous Conversion Options

The current price from AB Electronics is £15.99 (https://www.abelectronics.co.uk/p/69/adc-pi-raspberry-pi-analogue-to-digital-converter), although it has no connection blocks for that price and an additional £1.50 would be required to add these.
## ADC-DAC Pi Zero
This is a 2 channel 12 bit analogue to digital converter and 2 channel 12 bit digital to analogue converter pm a single module, which communicates with the Pi via an unspecified bus. No full specification appears to be provided, but ythe implications are that it is I2C. The A/D sample rate is considerably higher than the ADC Pi.
The current price from AB Electronics is £11.49 (https://www.abelectronics.co.uk/p/74/adc-dac-pi-zero-raspberry-pi-adc-and-dac-expansion-board), although it has no connection blocks for that price and an additional £1 or so would be required to add these. Unlike the ADC Pi, only one of these boards can be attached to a single Pi.
## Adafruit 4 Channel I2C 12-Bit Analogue to Digital Converter
This is a high-precision ADC and features the ADS1015 chip, which provides 12-bit precision at 3300 samples/second over I2C. It has the following specification:
- Wide Supply Range: 2.0V to 5.5V
- Low Current Consumption: Continuous Mode: Only 150µA Single-Shot Mode: Auto Shut-Down
- Programmable Data Rate: 128SPS to 3.3kSPS
- Internal Low-Drift Voltage Reference
- Internal Oscillator
- Internal PGA
- I2C Interface: Pin-Selectable Addresses
- Can run from 2V to 5V power/logic
- Measures a large range of signals and is super easy to use.
- 12-bit precision at 3300 samples/second over I2C.
- Configurable as 4 single-ended input channels, or two differential channels.
- Includes a programmable gain amplifier, up to x16, to help boost up smaller single/differential signals to the full range.
- Breakout Board equipped with ferrites to keep the AVDD and AGND quiet.
- Up to four boards on a single Pi.

The current price from ModMyPi is £9.95 (https://www.modmypi.com/raspberry-pi/iousbanalogue-expansion-1028/adcs-and-analogue-expansion-1030/adafruit-4-channel-i2c-12-bit-analogue-to-digital-converter-adc) and comes with a small connector block. Unlike the AB Electronics devices it is not designed to completely occupy the Pi’s GPIO connector so it could be easier to integrate with other devices.
## Adafruit 4 Channel I2C 16-Bit Analogue to Digital Converter
This is similar to the 12 bit version, but provides 16 bit resolution using the ADS1115 chip. The current price from Pimoroni is £13.20 (https://shop.pimoroni.com/products/adafruit-ads1115-16-bit-adc-4-channel-with-programmable-gain-amplifier). It is also available from Gearbest for £3.04 (https://www.gearbest.com/boards-shields/pp_343606.html?wid=1433363&currency=GBP&vip=4264385&gclid=EAIaIQobChMIm62Q2-2K3gIVD53tCh1CdAtaEAQYBSABEgJFlPD_BwE) (but with no support).
# PRACTICAL CONSIDERATIONS
## Building an Assembly from Components
As already mentioned above, building a A/D assembly using an A/D chip and associated components is likely to be more expensive than at first thought because of the cost of the circuit board, especially if a surface mount IC is used. This makes the cost of a Pre-packaged module more attractive.
## Interfacing to the Pi
The current System Design of the River System includes the use of a Master Pi and several Slave Pis, eg at the Wendy House, Railway and Gazebo Butts. This raise the question of how to connect anything up to 9 sensors to a Slave Pi, along with signals to control Gate Valves and Pumps. (This scenario could arise at the Railway Room Buts Farm(s) where it might be necessary to monitor and control the levels in three separate Butts Farms, each with three sensors and a Gate Valve.)
The idea of using a Serial Bus of some description has been under consideration for many months at the time of writing and some work has already been done by designing an I2C device into a Magnetic Probes Interface. However, that approach would then have to be in addition to the A/D Converter design, whatever is chosen. A more seamless solution is therefore desirable.
Bearing in mind that the various A/D module suppliers seem to concentrate on I2C for interfacing, this would seem to be the way forward; but how to integrate all the signals needed.
In addition, there is a potential problem in areas such as the Railway Room Buts Farm, whereby the sensors may be too far from the Pi for i2C to work, necessitating some form of buffering.
## A Radical Proposal
The following is offered a solution to this problem. In order to work the following constraints are imposed:
- All sensors provide an analogue signal to the interface (except float switches and flow sensors).
- All control signals are simple On/Off levels (eg, ‘1’ and ‘0’).

The radical proposal is that all sensors provide an analogue signal, but it should be relatively easy to convert the highs and lows from the Magnetic Levels Probe to a voltage proportional to the level. This voltage would then be read by the A/D in the module and passed to the Pi as a value. If the ADC Pi were used, (for example) up to 8 sensors could be monitored before problems occurred.
Float switches and control signals for the Gate Valves and pumps would then be routed to the 20 or so remaining GPIO Pins.
To overcome the distance issues; use will be made of the Pi Zero. This is version of the Pi that includes all of the basic functions, but costs only £4 or so. By utilising one Pi to interface to each A/D Module or Motor Drive Board, a great deal of complexity will be removed.
The diagram below shows how the solution might be implemented.