WIMBORNE MODEL TOWN DEVELOPMENT
STATEMENT OF REQUIREMENTS
FOR THE RIVER SYSTEM AESTHETIC IMPROVEMENTS
Issue 0.2
17th December 2017

This work is licensed under the Creative Commons Attribution-NonCommercial-ShareAlike 4.0 International License. To view a copy of this license, visit http://creativecommons.org/licenses/by-nc-sa/4.0/.

Annexes
A	Illustrations
B	Sensors Developed Prior to December 2017
# INTRODUCTION
This document details the requirements for aesthetic improvements to the river and its environs in Wimborne Model Town (WMT) to create a more natural looking representation of the River Allen which is a chalk stream. This Statement of Requirements is intended to provide a definition of the constraints that need to be taken into account while devising the required improvements.
Annex A of this document provides an Illustration that shows the configuration of the Model River and some of the associated elements of the River System. Section 2 of this document provides an description of this diagram.
The goal of this development is to add pebbles and other miscellaneous items to enhance the overall realism and aesthetic of the river and to provide a more suitable habitat for the insect and amphibian creatures that inhabit it.
There are some advantages and disadvantages of this proposal:

- Advantages:
  - It will improve the appearance of the WMT.
  - The gains would be quite high compared to the cost.
- Disadvantages:
  - The river could become more difficult to clean and maintain.
  - The improvements could restrict the flow of the water.
It is part of this requirement to address the disadvantages outlined above, and any others identified, within the documentation that accompanies the proposal.
## BACKGROUND TO THE REQUIREMENTS
Full details of the background to the Requirements for the enhancements to the river system as a whole may be found in Reference 1 in Section 1.2.
## Related Documents
The following documents are relevant to these Requirements.
Table 1: Related Documents

No	Requirement	Issue / Date
1	WMT River System Requirements	0.5
2	Wimborne Model Town Projects Forum	-
3	Met Office - Climate at WMT	-
4	Creative Commons Attribution-ShareAlike International License	4.0

## Definitions
River System	This term is used to describe all elements of the WMT model river and it’s associated control and monitoring components.
WMT	Wimborne Model Town

# RIVER SYSTEM LAYOUT
Figure 1 in Annex A shows the way in which the water is circulated within the river elements that are part of the WMT model, eg the Bog Garden and the two branches of the River Allen.
The Sump is located at the southern end of the river and contains approximately 1000 litres of water. A pump (the Sump Pump) recirculates this water through an underground pipe to the Bog Garden which is at the other end of the site, adjacent to the Main Entrance. Water then flows down the two river beds and back into the sump, turning the Water Wheel just before it re-enters the Sump. The Master Pi will control the operation of the Sump Pump to maintain the river flow based on the measured flow rate.
As a result of the filtration provided by the Bog Garden, the water in the river is considerably cleaner than it had been prior to its installation. Nevertheless, there is still many sources of material that dirty the water, mainly the fall of leaves in the Autumn. However, algal growth is still a problem and causes many hours of work for the gardeners.
Any solutions proposed as a response to these requirements need to take cognizance of this issue.
# FUNCTIONAL REQUIREMENTS
Table 3 below details the Functional Requirements for any aesthetic improvements to the WMT River System.
Table 2: Aesthetic Improvements Functional Requirements

No	Requirement
3.1	Aesthetic improvements shall be made to the WMT river.
3.1.2	Decorative features may be added to the river bed.
3.1.3	Decorative features may be added to the river banks.
3.1.4	Decorative features may be added to the surface of the river.

# MECHANICAL REQUIREMENTS
Table 5 below details the mechanical requirements for any any aesthetic improvements to the WMT.
Table 3: Mechanical Requirements for Aesthetic Improvements

No	Requirement
4.1	Any improvements added to the river shall be to the same scale as the rest of the WMT, see Note 1.
4.2	Any decorative features added under Requirements 3.1.2 to 3.1.4 inclusive shall not impede the overall flow of water in any significant way. Localised areas of fast flowing or slack water is acceptable.
4.3	Any improvements added to the river shall be heavy enough to remain in place during periods of high water flow or wind.
4.4	All materials used for the improvements shall be robust enough to resist erosion or corrosion.
4.5	Any improvements added to the river shall not trap algae or other debris to any significant extent.
4.6	The improvements shall not require significant regular maintenance or cleaning but recommendation on annual refurbishment should form part of the delivered documentation.

Notes:
1.	The WMT is a 1/10th scale model of the real town.
# NON-FUNCTIONAL REQUIREMENTS
## Environmental
Table 4 below details the environmental requirements for any aesthetic improvements to the WMT.
Table 4: Environmental Requirements

No	Requirement
5.1	The developer shall consider all environmental aspects when developing improvements.
5.1.1	Any proposed improvements shall be designed to remain attractive for a long period when exposed to the weather conditions expected at the WMT.
5.1.2	No improvement shall harm the environment.
5.1.2	It shall be possible to revert to the earlier configuration after the development has been completed.

Notes:
1.	The weather conditions at the WMT are assumed to be normal UK meteorological climate (see Reference 3 in Section 1.2).
## Documentation
The Table below details the documentation requirements for the aesthetic improvements.
Table 5: Documentation Requirements

No	Requirement
5.2	A comprehensive design document shall be produced (see Note 1).
5.2.1	The design document shall include a comprehensive list of all improvements.
5.2.1.1	The list shall include the materials used in each improvement.
5.2.1.2	The list shall include the approximate cost of each improvement.
5.2.2	The design document shall address the disadvantages set out in Section 1, putting forward mitigations for each, particularly the maintenance aspects.
5.2.3	All documentation shall be Copyright Wimborne Model Town and licensed under the Creative Commons Attribution-NonCommercial-ShareAlike 4.0 International License (see Reference 4 in Section 1.2).

Note 1: An example of a design document will be provided.
# ASSUMPTIONS
The following assumptions are made.
Developers will have the pre-requisite knowledge to design and implement the improvements required to realise this part of the project.
# SUMMARY OF CHANGES TO THIS DOCUMENT
The Table below details the changes made to this document for each revision.
Table 6: Summary of Changes to this Document

Issue	Section	Summary of Change
0.1	-	First draft.

ANNEX A – ILLUSTRATIONS

Illustration 1 – Main Main River and Sump Arrangement
Illustration 1: River System – Proposed Deployment – Main River and Sump Arrangement