WIMBORNE MODEL TOWN
DEVELOPMENT
RIVER SYSTEM REPLACEMENT NAS BOX REQUIREMENTS
Issue 0.1
4th August 2022

This work is licensed under the Creative Commons Attribution-NonCommercial-ShareAlike 4.0 International License. To view a copy of this license, visit http://creativecommons.org/licenses/by-nc-sa/4.0/.

# INTRODUCTION
This document details the requirements for a replacement Network Attached Storage (NAS) device to replace the current D-Link unit being used to store River System data at Wimborne Model Town.
## BACKGROUND TO THE REQUIREMENTS
In June 2019 it was decided that a better way to store readings and River System status information was needed. Previously distributed files on each Raspberry Pi had been used, but this resulted in difficulties assessing the data, especially when trying to compare readings at specific times. A D-Link DNS 320L NAS Box became available and this was configured to store the data in a database.
The exercise proved to be less than simple because the proprietary hardware in the device was running a very old copy of the Linux kernel and used a fairly obscure processor. A newer kernel was needed to allow a reasonably up to date version of the database software to be used. Since then, it has been found that there is no further upgrade path so some of the newer features of the OS and the database are unavailable. The lack of the ability to apply updates also increases the security risk, although the device is installed within a private network, with no access to the Internet except via a Virtual Private Network (VPN) Server.
The device is now six years old and there is concern that a failure in its electronics could render the device unusable. It has therefore been decided to explore the options for replacement. These include:
Table 1: NAS Box Options for Replacement
Solution	Advantages	Disadvantages
New Proprietary NAS Box	Relatively Easy to do if the Manufacture supports the device and keeps it up to date.	Very difficult to do and maintain if the Manufacture does not support the device and keeps it up to date. / Expensive.
Recycled Proprietary NAS Box	Dittto. / Cheap	Very difficult to do and maintain if the Manufacture does not support the device and keeps it up to date.
NAS Box Constructed from a recycled PC running an up-to-date version of Linux.	Easy to setup using the many articles, tutorials and videos on the Internet. / Cheap / The hardware can be replaced in the event of failure by replacing the recycled PC with a newer and more up to date one.	Noisy and Bulky.
NAS Box Constructed from a Raspberry Pi running an up-to-date version of Linux.	Relatively easy to setup using the many articles, tutorials and videos on the Internet. / The hardware can be replaced in the event of failure using off-the shelf and potentially newer Raspberry Pi versions.	There are no Raspberry Pi Versions at present that provide SATA or PCIe interfaces. / If USB is used, then data transfer rates might be unacceptably low unless a Pi with a recent USB interface was used. / Costs would be higher than using recycled devices but probably cheaper than a new NAS Box.

Assuming that it is decided to undertake the project, then the budgetary constraints of the WMT must be considered in any proposed solution.
## Related Documents
The following documents have been used as the source materials for these Requirements.
Table 2: Related Documents

No	Requirement	Issue / Date
1	WMT River System Design	0.5
2	WMT River System Sogtware Design	0.12

# DETAILED REQUIREMENTS
The following detailed requirements for the replacement NAS Box
## Functional
The functionality required of the replacement NAS Box are provided in Table 3 below.
Table 3: Functional Requirements

No	Requirement	Priority	Type
2.1.1	The replacement NAS Box shall provide storage for River System Readings and Status data.	1	Essential
2.1.1.1	The storage provided shall provide fail-over protection for the data such as RAID 1.	1	Essential
2.1.1.2	The storage provided shall be at least 100 GB	1	Essential
2.1.2	The replacement NAS Box shall run an up to date version of Linux.	1	Essential
2.1.2.1	It shall be possible to easily update the Linux software.	1	Essential
2.1.2.2	It shall be possible to easily update the Linux software.	1	Essential
2.1.3	The replacement NAS Box shall run a compatible version of the database on the current NAS Box.	1	Essential
2.1.3.1	It shall be possible to easily update the database software.	1	Essential
2.1.4	It shall be possible to run the existing WMT custom software on the replacement NAS Box	1	Essential
2.1.5	The replacement NAS Box shall be constructed from computer hardware that is easy to repair.	2	Desirable
2.1.6	The replacement NAS Box shall be constructed from computer hardware that is easy to upgrade.	2	Desirable

## Environmental
The Table below details the environmental requirements of the replacement NAS Box, their priority and type.
Table 4: Environmental Requirements

No	Requirement	Priority	Type
2.2.1	All electronic components of the system that are installed.	1	Essential
2.2.2	All electronic components shall be adequately cooled.	1	Essential

## Reliability
The Table below details the reliability required of the system, it's priority and type.
Table 5: Reliability Requirements

No	Requirement	Priority	Type
2.3.1	The replacement NAS Box shall be designed to be fail-safe in the event of a power supply failure.	1	Essential
2.3.2	Components shall be de-rated where possible, especially circuits carrying powers in excess of 1 W.	1	Essential
2.3.3	The replacement NAS Box shall use redundancy where possible to protect against hardware failures.	2	Desirable

## Maintainability
The Table below details the maintainability required of the replacement NAS Box, it's priority and type.
Table 6: Maintainability Requirements

No	Requirement	Priority	Type
2.4.1	The replacement NAS Box shall be designed to be maintainable by suitably qualified Town staff, using only the documentation provided by the developers.	1	Essential
2.4.2	Spares shall be provided for any components that are liable to end-of-life or frequent failure.	1	Essential
2.4.3	Backups of any software developed shall be made available for future maintainers.	1	Essential

## Safety
The Table below details the safety requirements of the system, it's priority and type.
Table 7: Safety Requirements

No	Requirement	Priority	Type
2.5.1	The replacement NAS Box must be designed such that elements of the system that use mains or high voltage supplies are fully protected to avoid the danger of electrical shock.	1	Essential
2.5.2	Power supplies derived from mains must be fully enclosed in a protective case.	1	Essential
2.5.3	Any heavy objects, such as a full size PC case, must be adequately secured to prevent inadvertent injury.	1	Essential

## Documentation
The Table below details the documentation requirements of the system, it's priority and type.
Table 8: Documentation Requirements

No	Requirement	Priority	Type
2.6.1	A comprehensive design specification shall be produced.	1	Essential
2.6.2	The design specification shall include full descriptions of all functionality, parts lists and circuit diagrams.	1	Essential
2.6.3	All software shall be fully documented with comments.	1	Essential
2.6.4	An Installation Specification shall be provided that details how to deploy the software and hardware.	1	Essential
2.6.4.1	A set of installation scripts shall be provided where possible to automate large parts of the software setup process.	2	Desirable
2.6.5	A User Manual shall be provided that details how to use and maintain the software and hardware.	1	Essential

## Miscellaneous
The Table below details the miscellaneous requirements of the system, it's priority and type.
Table 9: Miscellaneous Requirements

No	Requirement	Priority	Type
2.7.1	Where possible and without compromising the other requirements in this document, elements of the existing replacement NAS Box shall be re-used.	2	Goal
2.7.2.	The project team shall estimate the cost of the project, so that a budget may be agreed.	2	Goal
2.7.3	The project shall be developed in an agile manner so that the order of development may be varied to suit budgetary constraints and opportunities.	2	Goal

# ASSUMPTIONS
The following assumptions are made.
- Developers will have the pre-requisite knowledge to design and implement the hardware and software required to realise this project and subsequently enhance it.
- Maintainers will have the pre-requisite knowledge, supported by the supplied documentation, to maintain the system.
- WMT staff will have the pre-requisite knowledge, supported by the supplied documentation, to operate and monitor the system.