WIMBORNE MODEL TOWN DEVELOPMENT
STATEMENT OF REQUIREMENTS
FOR THE MOBILE RIVER SYSTEM VISITOR AND STAFF GUI
Issue 1.1
19th January 2021

This work is licensed under the Creative Commons Attribution-NonCommercial-ShareAlike 4.0 International License. To view a copy of this license, visit http://creativecommons.org/licenses/by-nc-sa/4.0/.

Annexes
A	Illustrations
# INTRODUCTION
** NEEDS UPDATING **
This document details the requirements for the Visitor and Staff Graphical User Interfaces (GUI). This GUI has two distinct functions but is primarily to allow visitors to view the operation and state of pumps, valves and sensors in the Wimborne Model Town (WMT) River feature. Additionally, as a subsidiary function, this GUI is required to provide control of the system for privileged users, ie the WMT staff. This development is intended to provide the following facilities:
- For Visitors:
  - Provide an attractive display of the operation of the system, based upon a graphical representation of the river and it’s components.
  - Display the level of water in the Sump and the various Butts Farms.
  - Display the flow rate of water in the river.
  - Show the state of the various valves and pumps in the system.
  - Show the direction of flow of the water in the pipes between the sump and the Butts Farms.
- For Staff:
  - Allow manual control of the system in the event of a problem occurring or a need to switch the system off temporarily.
  - Trigger and error message on the Visitor GUI to alert staff to issues occurring.
The GUIs should be a web based system to allow staff and visitors to monitor it from devices other than the main Visitor GUI screen, should this be required. Hardware requirements are not part of this document, but are described below to aid visualisation of the system.
Data will be generated by the functional software running on a number of Raspberry Pi computers, (see Reference 1 in Section 1.3) directly connected to the pumps, valves and sensors in the River System. One of these Pis (designated the Master Pi) will collect all the data together and make it available to the Visitor GUI software via Ethernet.
## BACKGROUND TO THE REQUIREMENTS
Full details of the background to the Requirements for the enhancements to the river system as a whole may be found in Reference 1 in Section 1.2.
## Related Documents
The following documents are relevant to these Requirements.
Table 1: Related Documents

No	Requirement	Issue / Date
1	WMT River System Requirements	0.5
2	GNU General Public License	3
3	TCP/IP	-
4	Creative Commons Attribution-ShareAlike International License	4.0

## Related Tools
The following tools are relevant to these Requirements.
Table 2: Related Tools

No	Requirement	Issue / Date
1	Raspberry Pi Computer	-
2	Hypertext Markup Language	5
3	Flask micro webdevelopment framework for Python (and any assoc’d modules)	Latest
4	Python Programming Language	Latest
5	Raspberry Pi Operating System	Latest (caveat: mysql library must support NAS box database)
6	JavaScript Framework for client-side decoration (TBD)	TBD
7	Mysqldb library	Latest (with caveat)

## Definitions
GUI	Graphical User Interface
HDMI	High Definition Multimedia Interface
HTML	Hypertext Markup Language
GUI Pi	The Raspberry Pi that is driving the Visitor and staff GUIs
master	The Raspberry Pi that is controlling the system.
remote	Any Raspberry Pi that is under the control of the master.
River System	All elements of the WMT model river and its control and monitoring components.
TCP/IP	Transmission Control Protocol / Internet Protocol
WMT	Wimborne Model Town

# HARDWARE CONFIGURATION
### Main River Circulation
** NEEDS UPDATING OR REFERENCE A DOCUMENT WHICH DESCRIBES IT **
Figure 1 in Annex A shows the way in which the water is circulated within the river elements that are part of the WMT model, eg the Bog Garden and the two branches of the River Allen.
The Sump is located at the southern end of the river and contains approximately 500 litres of water. A pump (the Sump Pump) recirculates this water through an underground pipe to the Bog Garden which is at the other end of the site, adjacent to the Main Entrance. Water then flows down the two river beds and back into the sump, turning the Water Wheel just before it re-enters the Sump. The Master Pi will control the operation of the Sump Pump to maintain the river flow based on the measured flow rate.
Also shown on this diagram is the configuration of the water collection system as of December 2017; this includes collection of water from the roofs of some of the buildings and storage in five water butts behind the Wendy Houses. These details should make it easier to understand the full description of this system in the next Section below.
It should be noted that the river and Bog Garden contain a combined total of some 15,000 litres of water, so if the Sump Pump stops for some reason then a large quantity of this water will continue to flow into the Sump, resulting in considerable water loss through the Soak-away.
### Water Collection
Figure 2 in Annex A shows the proposed layout of the water collection system.
Water collected from the buildings will either flow into the river or directly into water butts located at various points around the site. These water butts will be grouped together in sets of five butts, each designated with a Group Number. Water levels in the Sump and in each of the Butts Groups will be monitored and water will be pumped to and from Sump to ensure that it does not overflow into the Soak-away or run out of water during dry periods.
Each Butts Group will be monitored by sensors connected to a Raspberry Pi (a Remote Pi) and the Master Pi will decide when to operate valves and pumps to optimise water usage.
The Gardeners Butts Group at G5 will not be used to refill the Sump or take water from it. Instead, this Butts Group will provide water to ‘Leaky Hoses’ (and a manual tap) to water the gardens overnight, when water loss due to evaporation will be minimised.
### Raspberry Pi Computer
Full details of the Raspberry Pi computer may be found at Reference 1 in Section 1.3. Apart from being a fully specified computer, it also has a number of General Purpose Digital Input / Output (GPIO) lines which can be programmed to be discrete inputs, discrete outputs and (for some of the lines) serial interfaces. To interface to the GPIO lines, additional circuits may be required. Some work has been done on this and a description of the current capabilities is given in Annex B.
A display may be connected to the Raspberry Pi using the High Definition Multimedia Interface (HDMI) connector.
NOTE: It is not yet agreed which Raspberry Pi will host with webserver – it may be WMT-Webserver or a new dedicated Raspberry Pi.
### Display Specifications
Note:	At the time of writing these specifications are still being agreed because the WMT would like an outdoor (IP65) Touch Screen Display, but the budget currently doesn’t include this. Any Web GUI developed for this project must therefore be flexible enough to work with a variety of screens and interfaces as defined below:

Display Driver	Raspberry Pi providing a Web Browser interface into the standard HDMI port. This will be known as the GUI Pi.
Screen Size - IP65 (outdoor display)	12” to 19”.
Screen Size - (indoor display)	19” to 25”.
Visitor / Staff interface	Touch screen or / Mouse or / Trackball or / Five robust buttons connected to the Raspberry Pi GPIO pins (Cursor up, down, left, right and left click)

** NEED NOTES FOR MOBILES WE’RE TARGETING **
# GENERAL REQUIREMENTS
## Software Environment
### Visitor and Staff GUIs
The Visitor and Staff GUIs shall be implemented using code written in Hypertext Markup Language (HTML), (see Reference 2 in Section 1.3) Version 5 to carry scripts that generate and render the content. The preferred framework is Flask (see Reference 3 in Section 1.3) because it allows the Python Programming Language (see Reference 4 in Section 1.3) to be used for the scripting language. However, any fully cross-platform web framework may be used, providing that the languages and tools are open and free.
Note:	Python is preferred as the scripting language because it has been used to realise the software used for the other elements of this system and also for other Projects within the WMT.
The mobile interface will also depend on another language (such as JavaScript) for client-side decoration.
### Operating System
#### Development
Any Operating System may be used for development.
#### Deployment
The Operating System used for the deployed system will be Raspberry Pi OS, (see Reference 5 in Section 1.3) version Buster, running on a Raspberry Pi so any developed software shall be tested on that platform.
The client-side of the mobile interface will be accessible Android and iOS (versions TBD). For phones (and maybe also tablets).
### Copyright
All software will be Copyright Wimborne Model Town and Released under the GNU Public License (GPL) Version 3, (see Reference 2 in Section 1.3).
All documentation will be Copyright Wimborne Model Town and licensed under the Creative Commons Attribution-NonCommercial-ShareAlike 4.0 International License (see Reference 8 in Section 1.2).
## Communications
### Medium and Protocols
All communications between the Visitor GUI Pi and the Master Pi shall use Transmission Control Protocol / Internet Protocol (TCP/IP) (see Reference 3 in Section 1.2) over an Ethernet link (possibly supplemented by a wireless technology).
Mobile devices will need to connect over Wi-Fi.
### Methodology
** OUT OF DATE **

The Master Pi will host a database which will contain records of each River System data item. The GUI Pi shall read each record in turn before displaying the relevant reading or state on the display. The software on the GUI Pi will have permission to write to the database in order to transmit Staff commands to the Master Pi.
Visitor mobile devices will not talk direct to the NAS box database, instead communications will be via the web application server to improve security, and reduce load on the NAS box.
# FUNCTIONAL REQUIREMENTS
## Software Requirements for the Visitor Display
Table 3 below details the Functional Requirements for the Visitor GUI.
Table 3: Visitor GUI Functional Requirements

No	Requirement
4.1	The Visitor GUI shall provide a visual display of the state of the River System.
4.1.1	The Visitor GUI shall provide a level of detail appropriate for the zoom level.
4.1.2	The display shall consist of a graphical representation of the river (the Plan) and all of its elements, such as Butts, Sump, pumps and valves.
4.1.3	Each element of the Plan shall be represented by a graphical symbol that conveys its function to a non-expert viewer.
4.1.4	The graphical symbols for each element shall provide a representation of it’s state, and be animated where appropriate eg:
4.1.4.1	Each Valve element shall show whether it is open, closed or partially open.
4.1.4.2	Each Pump element shall show whether it is running or stopped.
4.1.4.3	Each Sensor element shall display its reading in terms of depth of water in the vessel or rate of water flow.
4.1.4.4	Each pipe element shall show the state of the water within it, eg stopped or flowing.
4.1.4.5	Where water is flowing within a pipe element, the Plan shall show the direction of flow.
4.1.5	A ‘fast replay’ feature should be provided to allow Visitors to watch the River System in Action during a recent weather event, such as prolonged rain or drought.
4.1.5.1	Make provision for the future addition of the ability to replay significant events.
4.1.6	It shall be possible for the Visitor or Staff member to select the required information from a Menu.
4.1.7	An ‘Information’ facility shall be included to explain in more detail how the River System works.
4.1.7.1	Upon interaction, more details can be shown about the state of individual elements.
4.1.7.2	Ability to navigate directly to any popups via an URL (for future provision of trail/guided tour)
4.1.8	Make future provision for localising all textual aspects of the interface.
4.1.9	Make provision for an audio/video guided tour of the web application.

Notes:
1.	Development of the Visitor GUI should pay cognizance to the Requirements detailed in Section 4.2 below.
2.	Requirement 4.1.5 is a stretch target and should be implemented only when all other requirements have been met.
## Software Requirements for the Staff Display
Table 4 shows the Functional Requirements for the GUI to be provided for WMT staff.
Table 4: Staff GUI Functional Requirements

No	Requirement
4.2	The Staff GUI shall provide a visual display of the operating state of the River System.
4.2.2	The display shall provide the same information as the Visitor GUI, supplemented by additional information and controls.
4.2.3	The Staff GUI shall be protected by a login system to prevent unauthorised access.
4.2.4	The Staff GUI shall provide the following additional controls:
4.2.4.1	Overall shutdown of the system.
4.2.4.2	Shutdown of individual segments of the system (eg, Group 1 Butts Pi).
4.2.4.3	Individual Control of the pumps.
4.2.4.4	Individual Control of the valves.
4.2.4.5	Control of the ‘fast replay’ feature detailed in Requirement 4.1.5.

Notes:
1.	Development of the Staff GUI should, if possible, utilise code developed for the Visitor GUI.
2.	Requirement 4.2.4.5 is a stretch target.
# NON-FUNCTIONAL REQUIREMENTS
## Operational
Table 5 below details the operational capabilities required of the software for both the visitors and staff. The GUI will be made available on site at WMT via a screen inside one of the rooms.
Table 5: Operational Requirements

No	Requirement
5.1.1	The Visitor GUI display shall be updated at frequent intervals to provide a dynamic experience for the Visitors.
5.1.2	The Staff GUI shall be accessible by use of a login with the aid of an external keyboard and mouse.
5.1.3	It is the responsibility of the Master Pi to enact control messages emitted by the Staff GUI, however, the Staff GUI display shall reflect the change in status within 1 second of the updated data being received.
5.1.4	The server should respond to all requests within 5 seconds.
5.1.5	The server should be able to handle simultaneous access by 50 visitors.

## Aesthetic and Ergonomic Requirements
Table 6: Aesthetic and Ergonomic Requirements

No	Requirement
5.2.1	The Visitor GUI display shall be provide an attractive and eye-catching view of the operation of the River System.
5.2.2	Careful attention should be paid to colour schemes when developing the Visitor and Staff GUIs.
5.2.3	Consideration should be given to the use of animation when representing elements of the River System.

Note:	It is recognised that the Requirements detailed in Section 5.2 are more aesthetic than technical but look and feel play a major role in drawing in and keeping the interest of the user. Some guidance on what may be appropriate is provided below:
  - Colours shouldn’t be too garish or too dull.

  - Colours should be chosen to provide the viewer with visual cues of what they represent’ ie blue may be chosen for water and so on. Also, pumps, valves and other elements could be colour-coded to make interpretation easier.
  - If animations are used, they shouldn’t be too overwhelming. Animations can rapidly become irritating if overdone.
## Documentation
The Table below details the documentation requirements for the Visitor and Staff GUIs.
Table 7: Documentation Requirements

No	Requirement
5.3.1	A comprehensive design specification shall be produced (see Note 1).
5.3.2	The design specification shall include high-level descriptions of all functionality of all components of the software.
5.3.3	All software shall be fully documented with comments.

Note 1: An example of a software design specification will be provided and it will be unnecessary for this document to provide detailed software documentation, provided that Requirement 5.3.3 has been adequately met.
# ASSUMPTIONS
The following assumptions are made.
Developers will have the pre-requisite knowledge to design and implement the software required to realise this part of the project and subsequently enhance it.
# SUMMARY OF CHANGES TO THIS DOCUMENT
The Table below details the changes made to this document for each revision.
Table 8: Summary of Changes to this Document

Issue	Section	Summary of Change
0.1	-	First draft.
0.2	-	DPJ comments
0.3	-	Comments from the Meeting on 19th Dec.
0.4	-	Changed styles to sans-serif and fixed some typos.
1.0	-	Accepted all review comments and corrected layout errors

ANNEX A – ILLUSTRATIONS

Illustration 1 – Main Main River and Sump Arrangement

Illustration 2 – Water Collection System
Illustration 1: River System – Proposed Deployment – Main River and Sump Arrangement

Illustration 2: River System – Proposed Deployment – Water Collection System