WIMBORNE MODEL TOWN
DEVELOPMENT
RIVER WEB-BASED CONTROL SYSTEM REQUIREMENTS
Issue 0.1
31st May 2023

This work is licensed under the Creative Commons Attribution-NonCommercial-ShareAlike 4.0 International License. To view a copy of this license, visit http://creativecommons.org/licenses/by-nc-sa/4.0/.

# INTRODUCTION
This document details the requirements for a Web-based Control System to allow staff and volunteers to manually control and monitor pumps, valves and sensors in the Wimborne Model Town River feature. This system is intended to take over from the currently implemented automatic control system when it is necessary owing to failure or unusual requirements. This version of the document covers the Requirements for the software to implement these features. This development is intended to:
- For the Sump and Wendy Butts:
  - Monitor the level of water in the sump and all of the butts.
  - Monitor the state of the float switch which indicates that they full. or empty
  - Switch on and off the pump used to transfer water from the sump to the five butts installed behind the Wendy House.
  - Show the state of the Wendy Butts Gate Valve and open and close it.
- For the Stage Butts:
  - Monitor the level of water in all of the butts.
  - Monitor the state of the float switch which indicates that they full. or empty
  - Show the state of the Gate Valve which controls the flow of water to the five butts installed behind the Wendy House and open or close it.
- For the Lady Hanham Butts:
  - Monitor the level of water in all of the butts.
  - Monitor the state of the float switch which indicates that they full. or empty
  - Show the state of any or all of the Gate Valves which control the flow of water to the fifteen butts installed behind the Wendy House and open or close them.
  - Show the state of the solenoid valve which controls the flow of mains water to the G1 Butts Group and open or close it.
- Re-use existing code and resources as much as possible.
Note:	The Visitor and Engineering GUI described in Reference 1.1.5 was originally intended to provide a graphical representation of the River System as an informative display for Visitors. The engineering part of this was intended to fulfil some of the functions described in this document.
## BACKGROUND TO THE REQUIREMENTS
At the time of writing, a shortage of volunteers with the necessary skills in software engineering has resulted in part of the existing automated system being incomplete, namely:
- The Stage Butts Control.
- The Lady Hanham Butts Control.
- The Water Backup System Control.
## Related Documents
The following documents are relevant to these Requirements.
Table 1: Related Documents

No	Requirement	Issue / Date
1	WMT River System Requirements	0.5
2	WMT River System Software Requirements	0.2
3	WMT River System Design	0.5
4	Overall System Configuration	0.12
5	Statement Of Requirements for the Mobile River System Visitor and Staff GUI	0.3
6	GNU General Public License	3
7	Creative Commons Attribution-ShareAlike International License	4.0

## Related Tools
The following tools are relevant to these Requirements.
Table 2: Related Tools

No	Requirement	Issue / Date
1	Raspberry Pi Computer	-
2	Hypertext Markup Language	5
3	Flask micro webdevelopment framework for Python (and any associated modules)	Latest
4	Python Programming Language	Latest
5	Raspberry Pi Operating System	Latest (caveat: mysql library must support NAS box database)
6	JavaScript Framework for client-side decoration (TBD)	TBD
7	Mysqldb library	Latest (with caveat)
8	NAS Box (D-Link DNS-320L)	N/A

## Definitions
GUI	Graphical User Interface
HDMI	High Definition Multimedia Interface
HTML	Hypertext Markup Language
Server	A computer or process that provides access to a resource over a network for other “client” devices or computers to use.
Web Server	The system that hosts the web pages used to access the visitor GUI.
Database Server	Stores and manages data from the River System, and makes it accessible to the Visitor and Staff GUIs.
River System	All elements of the WMT model river and its control and monitoring components.
NAS Box	Network-Attached-Storage system. This device holds the database that the river system uses to maintain state, and that will be used by the visitor and staff GUIs to display information.
TCP/IP	Transmission Control Protocol / Internet Protocol
WMT	Wimborne Model Town

# GENERAL REQUIREMENTS
The following general requirements have been identified.
## Hardware Configuration
References 3 and4 in Section 1.2 include diagrams showing the general arrangement of the hardware for the prototype deployment. Reference 5 in Section 1.2 provides an example of an earlier requirement that wasn’t completed.
The Control System shall be hosted on the WMT Web Server that provides the Visitor Audio Guides and Kiddies Quiz.
### User Device Specifications
Note: As WMT does not control which devices users may use to connect to the system, a range of display sizes and platforms must be accommodated. The system should be accessible on a ‘lowest common denominator’ of low end devices, in an attempt to ensure it will work well on all devices staff are likely to possess. This is of course limited by the availability of devices and compatibility of these devices with modern web technologies.
Operating System	IOS 6.1.6 or later, or Android 5.1 and later.
Form Factor	Mobile/handheld (but would be good to also work on tablets).
Screen size	3.5” or larger.
Screen resolution	720x1080 pixels or higher.
Other Capabilities	Mutli-touch support. / Support for HTML5, CSS3, and JavaScript (modern web technologies)

## Software Environment
The Operating System shall be Raspberry Pi OS.
### User Interface
The User Interface shall be implemented using code written in Hypertext Markup Language (HTML), (see Reference 2 in Section 1.3) Version 5 to carry scripts that generate and render the content. The preferred framework is Flask (see Reference 3 in Section 1.3) because it allows the Python Programming Language (see Reference 4 in Section 1.3) to be used for the scripting language.
Note:	Python is preferred as the scripting language because it has been used to realise the software used for the other elements of this system and also for other Projects within the WMT. Flask is the preferred framework because it has been used to develop the Minster Bells and Audio Staff Interface.
### Operating System
#### Development
Any Operating System may be used for development.
#### Deployment
The Operating System used for the deployed system for the Desktop interface will be Raspberry Pi OS, (see Reference 1 in Section 1.5) version Buster, running on a Raspberry Pi so any developed software shall be tested on that platform.
The client-side of the mobile interface will be accessible from Android and iOS (versions documented in Section 2.1.1). For phones and similar handheld devices.
### Copyright
All software will be Copyright Wimborne Model Town and Released under the GNU Public License (GPL) Version 3, (see Reference 6 in Section 1.2).
All documentation will be Copyright Wimborne Model Town and licensed under the Creative Commons Attribution-NonCommercial-ShareAlike 4.0 International License (see Reference 7 in Section 1.2).
## Communications
### Medium and Protocols
All communications between the Visitor GUI Pi and the Master Pi shall use Transmission Control Protocol / Internet Protocol (TCP/IP) over an Ethernet link (possibly supplemented by a wireless technology).
Mobile devices will need to connect over Wi-Fi.
### Methodology
The NAS box hosts a database which contains records of each River System data item, including current status and historical readings and events. The web server shall read each record in turn before presenting the data in an HTML page for the client to render. The software on the mobile devices will have permission to write to the database in order to transmit Staff commands to the NAS Box.
All communications between the hardware devices shall be via the Ethernet link already established for the automated system.
# FUNCTIONAL REQUIREMENTS
## Functional Requirements
The system shall present a web page to the operator, which will allow the functions described below to be selected.
## Presentation
To avoid overcrowding on moble devices the number of monitored functions and controls on each page shall be minimised as described below.
## General
Table 3: General Functional Requirements

No	Requirement
3.3.1	The display presented to the user shall provide information about the operating state of the River System.
3.3.1.1	The various levels of all of the Sump and all of the Butts Groups in the system shall be shown in the form of a non-editable number showing depth in mm.
3.3.1.2	The status of the Gate Valves shall be shown in the form of a non-editable number showing degree of opening in percent.
3.3.1.3	The status of the Butts Pum[p shall be shown in the form of a non-editable string indicating running or stopped.
3.3.1.4	The status of the mains solenoid valve shall be shown in the form of a non-editable string indicating open or closed.
3.3.2	The display presented to the user shall provide controls to allow the user to change the operating state of the River System.
3.3.2.1	User controls shall be positioned adjacent to the level or status that they directly effect.
3.3.8.2	Controls for the Butts Pump and Mains Solenoid Valve shall take the form of buttons labelled ‘On’ and ‘Off’.
3.3.7.3	Controls for Gate Valves shall take the form of an editable field to allow the percentage opening to be entered.
3.3.3	The Control System shall be protected by a login system to prevent unauthorised access.
3.3.4	It Control System shall provide a facility to fetch results from the database and copy them to the mobile device.
3.3.5	The Control System shall provide a button to affect shudown of any of the devices in the River System to allow power to be safely removed. (The Web Server itself is protected by an Uninteruptible Power Suppy and can therfore be shutdown simply by removing the power.)

Note:	Requirements 3.3.4 and 3.3.5 are stretch targets.
## Requirements for the Landing Page
Table 4: Landing Page Functional Requirements

No	Requirement
3.5.1	There shall be a ‘Landing Page’ with buttons and /or links to allow access to me detailed functions:
3.5.1.1	There shall be a Sump / Wendy Butts Page accessible from the Landing Page.
3.5.1.2	There shall be a Stage Butts Page accessible from the Landing Page
3.5.1.3	There shall be a Lady Hanham Butts Page accessible from the Landing Page.
3.5.1.4	There shall be a Device Shutdown Page accessible from the Landing Page.

## Detailed Requirements for Each Page
Table 5: Sump / Wendy Butts Page - Detailed Requirements

No	Requirement
3.5.3.1	The following Buttons shall be provided, each labelled with the associated function and adjacent to the monitored value that they control:
3.5.3.1.1	Sump Level and Butts Pump control.
3.5.3.1.2	Wendy Butts Level and Gate Valve Control.

Table 6: Stage Butts Page - Detailed Requirements

No	Requirement
3.6.4.1	The following Fields shall be provided, each providing the user with information about the associated status as detailed below:
3.6.4.1.1	Stage Butts Level and Stage Butts Gate Valve.
3.6.4.1.2.	Wendy Butts Level and Gate Valve Control.

Table 7: Lady Hanham Butts Page - Detailed Requirements

No	Requirement
3.7.4.1	The following Fields shall be provided, each providing the user with information about the associated status as detailed below:
3.7.4.1.1	Lady Hanham Butts Level for each Buuts Group (G1, G2 and G3) and Lady Hanham Butts Gate Valve for each Buuts Group.
3.7.4.1.2.	Solenoid Valve Control.

3.7.4.1.3.	Wendy Butts Level and Gate Valve Control.

## Operational
The Table below details the operational capabilities required of the software during the prototype deployment. Only developers will be required to access the system.
Table 8: Operational Requirements

No	Requirement
3.3.1	It shall be possible to monitor and control the system operation by logging in from a laptop or mobile phone.

## Documentation
The Table below details the documentation requirements for the software.
Table 9: Documentation Requirements

No	Requirement
3.5.1	A comprehensive design specification shall be produced.
3.5.2	The design specification shall include full descriptions of all functionality of all components of the software.
3.5.3	All software shall be fully documented with comments.

# ASSUMPTIONS
The following assumptions are made.
Developers will have the pre-requisite knowledge to design and implement the software required to realise this stage of the project and subsequently enhance it.
# SUMMARY OF CHANGES TO THIS DOCUMENT
The Table below details the changes made to this document for each revision.
Table 10: Summary of Changes to this Document

Issue	Section	Summary of Change
0.1	-	Initial issue for comments.