WMT River System Development
Comparison of Available Devices and Protocols
# Sensor Types
This is a subset of the variois sensor types that have been identified, but includes all of the viable types that do not cost more than a few tens of pounds to implement.
# Note: Analogue to Digital Converters (A/Ds) are available as detailed in the Section on Sensor Interfaces below. Unless a home made A/D is employed the costs of the commercial types must be added to the prices given in the Table below.
Device - >	HC-SR04	Probe Rods	Capacitance	Float	Pressure	Weight
Type	Level	Level	Level	Level	Level	Level
Technology	Ultrasonic Range	Conduction	Change of C	Microswitch	Air pressure	Weight of Butt
Pros	Cheap, simple, linear, existing Libraries	Cheap, simple, can use GPIO	Fairly cheap	Cheap, simple, can use GPIO	Fairly cheap, linear.	Fairly cheap, linear.
Cons	Difficult to protect from moisture/ice.	Coarse Measurement	Needs RF stimulus	Coarse Measurement	Needs pre-amp and A/D	Needs pre-amp and A/D
Price	£1.57	Home-made. A few poinds for materials.	Home-made; cost difficult to estimate.	£5 to £25, depending on the number of floats.	~£10 + A/D.	~£10 + A/D.

# Sensor Types Continued

Device - >	VL53L0X	Paddle	Paddle	Vane
Type	Level	Flow	Flow	Flow
Technology	Laser Range Finder	Hall Effect	Tacho-gen	Potentiometer
Pros	Linear, existing Libraries	Linear	Linear	Simple, cheap
Cons	Difficult to protect from moisture/ice		Probably have to make generator.	Non-linear, pot can wear. Needs A/D
Price	£15	~£5	?	~ £1 + A/D

# Devices for Sensor Interfaces and Data Processing

Device - >	Raspberry Pi Zero	Raspberry Pi 3	Arduino Uno	ADC Pi Plus	ADC Pi Plus	RaspIO Analog Zero
Microcontroller	BCM2835	BCM2837 (Quad Core)	Atmega328	NS	Ditto	Ditto
Operating Voltage	5 V	5 V	5V	GPIO Header	Ditto	Ditto
Input Voltage (recd)	N/A	N/A	7-9V	NS	Ditto	Ditto
Input Voltage (limits)	N/A	N/A	6-20V	NS	Ditto	Ditto
Digital I/O Pins	26	26	14 (6 provide PWM)	GPIO (pass through)	Ditto	Ditto
Analogue Input Pins	0	0	6	8	Ditto	Ditto
Analogue Voltage Range	N/A	N/A	0 to 5 V (can be extended)	0 to 5 V	Ditto	0 to 3.3 V
Resolution (bit)	N/A	N/A	10	17	Ditto	10 (can ext to 12)
Conversion time	N/A	N/A		240 SPS	Ditto	NS
DC Current per I/O Pin	N/A	N/A	40 ma	2 mA	Ditto	NS
DC Current for 3.3V Pin	N/A	N/A	50 mA	N/A	Ditto	NS
Flash Memory	N/A	N/A	32 KB (0.5 KB bootloader)	N/A	Ditto	Ditto
SRAM	512 MB	1 GB	2 KB	N/A	Ditto	Ditto
EEPROM	NS	NS	1 KB	N/A	Ditto	Ditto
Clock Speed	1 Gb/s	1.2 Gb/s	16 MHz	NS	Ditto	Ditto
Other Features	HDMI, 1 USB Port, Camera Port	HDMI, 4 USB, Port, Camera Port, Audio Jack	2 hardware Interupts, 6 8-bit PWM O/Ps	On board Programmable Amplifier (up to 8 X)	Ditto	Small prototyping area.
Comms	1-Wire, I2C, SPI, GPIO	1-Wire, I2C, SPI, GPIO, Ethernet, 802.11n WiFi	UART, I2C, SPI	I2C	Ditto	SPI
Price	£4	£30	£11	£15.99	£14.99	£10

# Dual Slope Analogue to Digital Converter
The last three items in the table in the previous Section are all traditional Aanalogue to Digital converters. They make it easy to code the functions, because support Libraries are provided. A cheaper alternative could be to use a single or dual-slope converter, as was used in traditional DMMs.

In this device, an analogue integrator is used with switched inputs, a comparator, and a counter unit. The input voltage is integrated for a fixed time interval (TCHARGE) that usually corresponds to the maximum count of the internal counter unit (Figure 4). At the end of this interval the device resets its counter and applies an opposite-polarity (negative) reference to the integrator input. With this opposite-polarity signal applied, the integrator "deintegrates" until its output reaches zero, which stops the counter and resets the integrator.
Charge gained by the integrator capacitor during the first, integrating/charging interval (TCHARGE/|VIN|) must equal that lost during the second, deintegrating/discharging interval (TDISCHARGE/|VREF|). Then the binary output is proportional to the ratio of these time intervals relative to the full count. TDISCHARGE at the end of the second interval corresponds to the ADC's output code.
Fuller details of the technique may be found at Analogue to Digital Converters.
The electronics could be realised using Op-amps and analogue multiplexers (for dual-slope) with on-board or external clocking. The Pi could be used to count the time and calculate the voltage and therefore the level. Alternatively, the Pi could simply trigger the measurement and read the count on its I/O pins.
This may end up more expensive than the bought-in A/D boards, but would be more educational.